## Slide 1: Selected Topics on the IoT
CoAP Reliability

## Slide 2: Reliability with CoAP
CoAP over UDP: No reliability at the transport layer
Messages can be (‘T’ header field - 2 bits):
  0: Confirmable (CON)
  1: Non-Confirmable (NON)
  2: Acknowledgements (ACK)
  3: Reset
CoAP also does some congestion control

## Slide 3: Piggybacked Response
          ACK 2.05 Content
          text/plain
          25.38C
(Time)
    CON GET /temp
The ACK is sent inside the response!

## Slide 4: Packet Loss
        T=ACK CODE=2.05 Content
        text/plain
        25.38C
(Time)
    CON GET /temp
    T=CON CODE=GET /temp
X
Timeout

## Slide 5: Separate Response
CON 2.05 Content Token=0x31 MID=0x345A
application/json
{"chip":{”VDD":2.98,"temp":36.78},"RF":"Pass"}
(Time)
    CON GET /diagnostic Token=0x31 MID=0xABCD
Maybe Dealing with the Request will take a while (Examples?)
          ACK MID=0xABCD
Process
          ACK MID=0x345A

## Slide 6: Request/Response Matching
(Time)
Q: If client sends multiple requests, how does the client know what response is for which request?
A: Tokens. Same token in request/response
CON 2.05 Content Token=0x31 MID=0x345A
application/json
{"chip":{”VDD":2.98,"temp":36.78},"RF":"Pass"}
    CON GET /diagnostic Token=0x31 MID=0xABCD
          ACK MID=0xABCD
          ACK MID=0x345A