## Slide 1: Selected Topics on the IoT
CoAP Observations and Blockwise

## Slide 2: CoAP Observe
Allows a client to subscribe for notifications
Server sends updates
Q: What triggers an update?
A: Mainly determined by the logic on the server and is resource-dependent. The client can request a fresh value at will (see Max-Age option later)
Examples (Combinations are possible):
Periodic (e.g. every X secs/mins)
Sudden change (e.g. reading is +/- 10% compared to previous reading)
Thresholds (e.g. reading is outside a normal range)

## Slide 3: Observe Example
(Time)
CON GET /temp Observe=0 TOKEN=0x31
ACK 2.05 Observe=3 TOKEN=0x31 <data>
ACK TOKEN=0x31
NON 2.05 Observe=4 TOKEN=0x31 <data>
CON 2.05 Observe=5 TOKEN=0x31 <data>
CON GET /temp Observe=1 TOKEN=0x31
Register: Observe=0
Server can use CON to check observer still there
Deregister: Observe=1
ACK 2.05 Observe=45 TOKEN=0x31 <data>

## Slide 4: CoAP Observe – Max-Age
With each OBSERVE, the server is allowed to include the Max-Age option in the header
This gives a hint to the client as to how long (in seconds) the value should be considered valid. Default 60 secs if Max-Age missing.
The client:
Must assume the last reading is no longer valid if it is older than Max-Age
Should not send a GET request for a fresh value before Max-Age expires (current value still valid!)
May refresh the observation after Max-Age (+ random time in [5 , 15] secs)

## Slide 5: Blockwise Transfers
Handling long messages
Remember: Constrained Networks!
  IEEE 802.15.4: max message 127 bytes at layer 2.
Message is transferred across multiple request/response pairs
Blockwise specified in a separate IETF document. All you need to know is that it exists.