## Slide 1: Optical Networks [EENGM0003]
Dr. George T. Kanellos
[gt.kanellos@bristol.ac.uk]

## Slide 2
Client layers of the optical layer

## Slide 3: WDM Optical Transport Networking
What is WDM Optical Networking?
  Transport Networking at a new level of granularity--the Optical Channel (OCh) Level: OCh-level routing and switching (i.e., beyond simple pt-to-pt WDM systems)
  Managing optical frequency-slots (OCh’s)
To create a new transport layer (the Optical Transport Network) requires building transport layer functionality into the Optical Layer
To Network Optical Channels requires an ability to manage Optical Channels
OCh-level OAM (Operations, Administration, Maintenance) information will be needed to support Optical Networking applications

## Slide 4: OSI model
A pipe that provides “bandwidth”to the data link
Framing/MUX/DEMUX/MAC
Ethernet
PPP
End-to-end routing
IP
In-sequence, error free messages
TCP

## Slide 5: IP over SONET

## Slide 6: The optical layer
Client layers
Second gen. optical networks  optical layer provides lightpath services

## Slide 7: Client layers to be discussed
SONET/SDH
- - 1st gen backbone optical networks (for low speed voice -51Mb/s)
Provides managed, end-to-end circuit switched connections
Efficient Time-division multiplexing
Supports data network and packet traffic
Optical Transport Network
Builds on SONET/SDH principles
Carries all types of data traffic
Very high transmission rates
Complete set of operation/management features

## Slide 8: Multiplexing in optical communication [Optical-ETDM]
Number of lower speed (baseband) sub-channels multiplexed in time domain using electronics forming aggregate (total) signal
This electrically multiplexed signal then converted into optical form in the transmitter
Bellcore came up with Synchronous Optical Network (SONET) while ITU in Europe came up with Synchronous Digital Hierarchy (SDH)
  SDH based on 155.52Mbit/s
  SONET based on 51.84Mbit/s

## Slide 9: The SONET/SDH Hierarchy
Optical SONET SDH Data rate Overhead rate Payload rate
level level level (Mbps) (Mbps) (Mbps) (electrical) (electrical)
OC-1 STS-1 ---- 51.84 1.728 50.112 OC-3 STS-3 STM-1 155.52 5.184 150.336 OC-12 STS-12 STM-4 622.08 20.736 601.344
OC-48 STS-48 STM-16 2488.32 82.944 2405.376
OC-192 STS-192 STM-64 9953.28 331.776 9621.504
OC-768 STS-768 STM-256 39,814.32 1327.104 38486.016
Electrical side of a SONET signal is a Synchronous Transport Signal (STS)
Electrical side of a SDH signal is a Synchronous Transport Module (STM)
Optical side of a SDH/SONET signal is an Optical Carrier (OC)
SDH basic rate (higher than SONET) – chosen to accommodate the commonly used PDH signals

## Slide 10: SDH Frame Structure
The STM-1 frame is the basic transmission format for SDH. The frame lasts for 125µs (= 1/8kHz sampling rate). Therefore, there are 8000 frames per second.
The STM-1 consists of overhead plus a virtual container capacity.
First nine columns of each frame make up the section overhead and the last 261 columns make up the Virtual Container capacity. The VC plus the pointers (H1, H2, H3) is called the Administrative Unit (AU).
The STM frame is transmitted in a byte-serial fashion, row-by-row.

## Slide 11: Frame Structure Synchronous Transport Module (STM-1)
9 rows
9 columns
270 columns
125µs
Repetitive frame structure with a periodicity of 125µs, the same as that of primary rate (E1)
9 x 270 = 2430 bytes in 125µs ie 2430 x 8 * 8000 = 155.52Mbit/s aggregate bit-rate
9 x 261 = 2349 bytes in 125µs ie 2349 x 8 * 8000 = 150.336bit/s useful payload per frame
Transport overhead (3%)
Usual Representation
Byte-wise Representation
64kbit/s

## Slide 12: SDH/SONET Network Elements
Add/drop multiplexer (ADM)
  Drops entire multiplexes
Terminal multiplexer (TM)
  Multiplexes traffic to different multiplexing hierarchies
Digital cross-connect (DXC)
  Switches virtual containers (VCs) between ports
Regenerator
  Deployed when distance > 40-60km in order to “clean-up” the signal
NxN

## Slide 13: Typical SDH/SONET Network
Ring A
Ring B
ATM Switch
ATM Switch
IP Router
IP Router
DXC interconnects rings
Point to point segment
Tributary Interfaces
Trunk Interfaces
ADM
ADM
ADM
ADM
ADM
ADM
TM
TM
Regenerator

## Slide 14: SDH/SONET Layers Terminology
The SDH layer consists of three sub-layers: the path, line and section
The SDH framing structure defines overheads operating at these layers (except photonic layer) to estimate error rates, communicate alarm conditions and provide maintenance support.
These overhead bytes are added whenever the layer is introduced and removed (when the layer is terminated in a network element).
Section
Line
Path
line
ADM
PTE
PTE
ADM
ADM
PTE
TM
PTE
Section
TM
Regenerator
Regenerator
Remember that these SDH layers are within layer 1 (physical layer) of the OSI model

## Slide 15: SDH/SONET Layers Terminology
The Path Layer is responsible for end-to-end connections between nodes and is terminated ONLY at the ends of an SDH connection.
The Line layer multiplexes a number of path-layer connections onto a single link between two nodes. Terminated at each intermediate terminal multiplexer (TM) or add/drop multiplexer (ADM).
The Section layer are the links between regenerators and the regenerator section is terminated at each regenerator in the network.
The Photonic Layer is responsible for transmission of bits across the fibre.
Photonic
Regen S
M S
Path
Photonic
Regen S
Photonic
Photonic
Regen S
Photonic
Regen S
M S
Path
Regen S
ATM Switch/ IP Router
ATM Switch/ IP Router
SDH Digital Cross- Connect (DXC)
Regenerator
SDH Digital Cross- Connect (DXC)
M S
M S

## Slide 16: Building SDH Core Networks Increasing capacity in “fibre-rich” networks
3
Increase capacity by “stacking” SDH Rings (Space Division Multiplexing)
1
2
Fibres
STM-x rings
STM-x ring
ADM
“Grey” trunk interfaces (1310nm)
n

## Slide 17: Building SDH Core Networks Increasing capacity in “fibre-poor” networks
Physical Layer
Fibre
Increase the bit rate
SDH/SONET
Higher Network Layers
Fibre
Increase the transmission bit-rate and multiplex more tributaries onto fibre eg Replace STM-16 (2.5Gbit/s) interfaces with STM-64 (10Gbit/s) interfaces

## Slide 18: Building SDH Core Networks Enhancing SDH with WDM
WDM
“coloured” interfaces
WDM transport
Physical Layer
Single fibre can typically carry up to 160x10Gbit/s channels (wavelengths)
Now being integrated into SDH equipment
SDH/SONET
Higher Network Layers
Fibre
Wavelength muliplexer/demutliplexer
Transponder (colour to grey)
(Optical-to-electrical-to-optical - OEO)

## Slide 19: Building SDH Core Networks Enhancing SDH with WDM
l3
Stacked SDH Rings within a fibre reduces problem of “fibre exhaustion”
l2
Wavelengths
STM-x rings
STM-x ring
l1
ADM
“coloured” trunk interfaces (15xxnm)
Wavelength determined by channel
ln

## Slide 20: Opaque Transport Networks: Separate Switching/Transport systems
  Conventional method since usually different vendors for WDM transport and switching/ routing equipment (preventing integration)
  Large number of intermediate back-to-back “grey” interfaces between the transport and switching systems.
  Configuration is very static and must be manually reconfigured if the percentage of local/transit traffic changes. Very important to get the traffic forecast correct when designing the network.
  Standard optical patch panels allow manual reconfiguration (slow and prone to errors)
Grey interfaces (1310nm)
WDM interfaces (15xxnm)
Transit traffic
Transponder (Optical to electrical to optical - OEO)
Clients
Patch panel
Switching/ Routing
WDM Transport
Local traffic (add/drop)
l1
l2
l3
l1
l2
l3
Switch/ Router
Building SDH Core Networks: Separate WDM Transport and SDH Network Elements

## Slide 21: Opaque Transport Networks: Integrated Switching/Transport systems
  Improves the dynamics of the network and allows the network operator to change the percentage of local/transit traffic at each node (according to changing traffic conditions)
  Switches/routers incorporate WDM interfaces - reduce the number of intermediate “grey” interfaces and eliminates intermediate “grey” interfaces and provides maximum flexibility
  All traffic must go through the electrical matrix - significantly increasing the size and cost (especially for nodes that have a large amount of transit traffic).
Clients
Switch/ Router
Grey interfaces (1310nm)
WDM interfaces (15xxnm)
Integrated switching/routing and WDM Transport
l1
l2
l3
l1
l2
l3
Building SDH Core Networks : Integrated SDH and WDM Transport

## Slide 22: End of part 1

## Slide 23: Optical Networks [EENGM0003]
Dr. George T. Kanellos
[gt.kanellos@bristol.ac.uk]

## Slide 24: Client layers to be discussed
SONET/SDH
- - 1st gen backbone optical networks (for low speed voice -51Mb/s)
Provides managed, end-to-end circuit switched connections
Efficient Time-division multiplexing
Supports data network and packet traffic
Optical Transport Network
Builds on SONET/SDH principles
Carries all types of data traffic
Very high transmission rates
Complete set of operation/management features

## Slide 25: Transparent (All-Optical) Transport Networks: 1st stage: Ultra-Long-Haul (ULH) systems
Ultra-long-haul systems are designed to have a long-reach between regenerators (>1500km typically). Typical reach of conventional WDM system is 500-700km.
The transparency range (TR) - also known as maximum transmission distance (MTD) - is the distance an optical signal can propagate without undergoing regeneration.
Longer TR = fewer OEO converters = lower cost network.
Destination terminal distance > Transparency range (TR)
Ultra-long-haul (ULH) WDM interfaces (OEO)
Back-to-back ULH transponders for regeneration
Patch panel
l3
l3
Clients
l3
Clients
l3
Terminal A
Terminal B
Could also change wavelength if necessary here

## Slide 26: Transparent (All-Optical) Transport Networks: 2nd stage: Optical by-pass of transit traffic
  Eliminates back-to-back transponders on through traffic at intermediate nodes = cost reduction
  Offers the benefit of eliminating superfluous interfaces (including back-to-back transponders for transit wavelengths)
  Reduces electrical matrix size, foot print, power consumption, interface count, etc.
Clients
Static optical add/drop multiplexer (OADM)
ADM/DXC
l1
l2
l3
l1
l2
l3
Patch panel
Grey interfaces (1310nm)
WDM interfaces (15xxnm)

## Slide 27: Agile Transparent Optical Transport Networks
  Optical switches provide dynamics at the optical wavelength level with all the benefits of optical transparency
  Reduces electrical matrix size, foot print, power consumption, interface count, etc.
  More complicated network design
Clients
Optical switch fabric
Switch/ Router
Grey interfaces (1310nm)
ULH WDM interfaces (15xxnm)
Reconfigurable optical OXC
Building SDH Core Networks All-optical switching in the WDM layer
  More complicated network design

## Slide 28: Optical Cross Connect Integration with Electronic Domain (IP and SDH)
Opaque Networks
  Optics used for high capacity transmission in a point-to-point fashion
  All the switching and other intelligent network functions handled by electronics (eg. SDH/SONET, IP/MPLS…)
  High cost of optical-to-electrical-to-optical (OEO) converters, especially at high bit-rates
Transparent (or all-optical) Networks
  Attempts to minimise the number of OEO converters in the network. Results in fewer OEO converters (lower CAPEX), reduced floor space and power consumption (lower OPEX)
  1st stage: Development of ultra-long-haul (ULH) systems provides longer reach between regenerators
  2nd stage: Optically by-pass traffic passing through the node instead of electrical processing
Agile Optical Networks
  Provides the ability to rapidly set up and take down lightpaths as required (dynamic)
  Agile opaque networks: use electrical switch fabric – reality now
  Agile transparent networks: complexities at physical layer (eg. adaptive power and dispersion management) need to be resolved before widespread deployment

## Slide 29: The Optical Transport Network Digital wrapper (G.709)
Fibre
SDH
ATM
IP
Ethernet
Optical Transport Network (OTN)
WDM
Digital Wrapper (ITU G.709)
“Wrap” electrical client into frames with additional overhead for OTN signalling and error correction capability (for increased transmission distance).
Electrical clients

## Slide 30: Optical Layers Defined
Optical Transport Network Layers:
OCh (optical channel) layer network provides end-to-end networking of optical channels for transparently conveying SDH, IP
OMS (optical multiplex section) layer network provides functionality for networking of a multi-wavelength optical signal
OTS (optical transmission section) layer network provides functionality for transmission of optical signals on optical media
SONET/SDH
{
Optical Channel (OCh) Layer
Optical Multiplex Section (OMS) Layer
Optical Transmission Section (OTS) Layer
Optical Layers
Digital Client Layers
{
ATM
Ethernet
IP
FC
etc.
Optical Interfaces

## Slide 31: Optical Layers Defined
A
T
M
O
C
h
S
O
M
S
O
T
S
O
C
h
S
O
M
S
O
T
S
O
T
S
O
T
S
O
M
S
O
T
S
O
T
S
:
O
p
t
i
c
a
l
T
r
a
n
s
m
i
s
s
i
o
n
S
e
c
t
i
o
n
O
M
S
:
O
p
t
i
c
a
l
M
u
l
t
i
p
l
e
x
S
e
c
t
i
o
n
O
C
h
S
:
O
p
t
i
c
a
l
C
h
a
n
n
e
l
S
e
c
t
i
o
n
S
D
H
I
P
A
T
M
S
D
H
I
P
Management of the quality
of the optical paths
Optical fiber
O
C
h
S

## Slide 32: Physical Significance of Layers
Amplifier
Wavelength cross - connect
(or add-drop mux)
Amplifier
SDH/IP
interface
SDH/IP
interface
Wavelength
multiplexer
Optical amplifier
sections
Optical amplifier
sections
Optical multiplex
section
Optical multiplex
section
Optical channel
Regenerator section
Notes: WDM network can be managed in the same way as a digital network

## Slide 33: OTN line rates and key additional features
Forward error correction: 7% higher line rate
Management: OTN allows up to 6 tandem connections monitoring
Protocol Transparency: all types of packet traffic (10GEthernet, IP) and SONET/SDH frames
Asynchronous timing:
OTN payload floats within the frame to account for client clock mismatch

## Slide 34: OTN hierarchy

## Slide 35: OTN Network Layers OTH Interface Structure

## Slide 36: The Optical Transport Module

## Slide 37: Optical Channel Data Unit (ODU)
The ODU is the single channel end-to-end network entity of the Optical Transport Network OTN
The ODU is terminated at the border of the OTN
The ODU consists of Optical Channel Payload Unit OPU and the ODU overhead for supervision & management
  Trace for connectivity supervision (Path monitoring)
  Support of nested tandem connection monitoring
  Automatic Protection switching (APS) to protect against circuit failures. When a circuit or router fails, a backup immediately takes over.
  Data communication channels (DCC) to access network devices for management access

## Slide 38: Optical Channel Data Unit (ODU) Frame Format
Frame format identical for all bit rates
The frame time depends on the bit-rate

## Slide 39: Optical Channel Data Unit (ODU) Performance Monitoring/Tandem Connection Monitoring (PM/TCM)
Operator A
Operator B
Operator A
User
Working
Protection
end-to-end path supervision (PM)
user QoS supervision (TCM1)
lead operator QoS supervision (TCM2)
protection supervision (TCM4)
domain and domain interconnect supervision (TCM3)
User
Start of the OTN
Client mapping into ODU
Border of the OTN
Client mapping into ODU

## Slide 40: End of session 8
Any questions?