## Slide 1: Optical Networks [EENGM0003]
Dr. George T. Kanellos
[gt.kanellos@bristol.ac.uk]

## Slide 2: Session 9
Optical network control and management system

## Slide 3: Optical network control and management system
Optical Network Control Plane
MPLS
GMPLS
Optical Network Management
Routing and Wavelength Assignment
Optical Network Survivability

## Slide 4: Control Plane Functions
Routing - Intra-domain and Inter-domain
  1) automatic topology and resource discovery
  2) path computation (How do we use the infrastructure)
Signaling - standard communications protocols between network elements for the establishment and maintenance of connections
Neighbor discovery - NE sharing of details of connectivity to all its neighbors (very powerful tool)
Local resource management - accounting of local available resources

## Slide 5: Control Plane : Distributed VS Centralized
Distributed Control:
  Distributed control infrastructure and intelligence that controls the establishment and maintenance of connections in the network, including protocols and mechanisms to disseminate this information; and algorithms for engineering an optimal path between end points
Centralized Control:
  Centralized control plane mechanisms supporting the above functionalities in a centralized way relying on client/ server model, usually involving one or more management applications (structured hierarchically) communicating to each network element in its domain

## Slide 6: Control Plane : Distributed VS Centralized
Centralized Control Plane
  Easier to implement
  Single point of failure
  Is not scalable with Size of network
  Provisioning
Centralized Control Plane
(Hierarchical )
NE
NE
NE
Distributed Control
Plane
NE
NE
NE
Protocols
Protocols
Distributed Control Plane
  Robust
  More Complex
  Scalable
We Discuss Distributed Control plane here

## Slide 7: Why IP over WDM?
It is widely believed that IP provides the only convergence layer in the global and ubiquitous Internet
  Most of the data traffic across network is IP
    Nearly all the end-user data application uses IP
    Conventional voice traffic can also be packetised with voice-over-IP
DWDM optical networks can address the continuous growth of the Internet traffic by exploring the existing fibre infrastructure

## Slide 8: Problem Statement
Problem:
  How to control and manage such an “All-IP” OTN network

## Slide 9: MPLS
MPLS stands for: “Multi-Protocol Label Switching”
Goals:
  Is considered a 2,5 layer protocol
  Bring the speed of layer 2 switching to layer 3
  Resolve the problems of IP over ATM, in particular:
    Complexity of control and management
    Scalability issues
  Support multiple layer 2 technologies (SONET/SDH, ATM, Ethernet)
  Allows for traffic engineering

## Slide 10: Basic Idea
MPLS is a hybrid model adopted by IETF to incorporate best properties in both packet routing & circuit switching
Forwarding:
Label Swapping
Control:
IP Router
Software
Control:
IP Router
Software
Forwarding:
Longest-match
Lookup
Control:
ATM Forum
Software
Forwarding:
Label Swapping
IP Router
MPLS
ATM Switch
Notes: Internet Engineering Task Force

## Slide 11: MPLS
Initially designed for packet switched electronic networks
To improve performance and scalability
  Traffic Engineering (put the traffic where the bandwidth is)
To be link layer independent
  To work transparently with existing L2 switching protocols
To be network layer independent
  To coexist with native: routing (IP) and switching (ATM)
To support services beyond best-effort
To support “aggregate forwarding”
  streams of data to be forwarded as a single entity between LSR
To support future Applications
  Universal Control Plane

## Slide 12: What is Label Switching?
In a traditional IP network:
  Each router performs an IP lookup (“routing”), determines a next-hop based on its routing table, and forwards the packet to that next-hop.
MPLS does “label switching” instead:
  The first device does a routing lookup, just like before
  But instead of finding a next-hop, it finds the final destination router.
  And it finds a pre-determined path from source to that final router.
  The path is called LSP: Label-switched Path
  The router applies a “label” based on this information.
  Subsequent routers use the label to route the traffic without needing to perform any additional IP lookups.
  At the final destination router the label is removed.

## Slide 13: MPLS Principle: The Label Information Base
Labeled packet arrives at Port 1, with Label value "5“
LSR extracts label and uses it to index into the forwarding table
Label entry indicates switch to Port 4
and swap label to value "7"
Connection Table
In
(port,Label)
Out
(port, Label, Operation)
(1, 5)
(1, 3)
(1, 17)
(2, 3)
(4, 7, Swap)
(4, 27, Swap)
(4, 123, Swap)
(3, 17, Push)
Port 1
Port 2
5
7
Port 3
Port 4
Label switched router
Label forwarding table

## Slide 14: MPLS Labels
Label: Label Value, 20 bits (0-16 reserved)
Exp.: Experimental, 3 bits (Class of Service is one use)
S: Bottom of Stack, 1 bit (1 = last entry in label stack)
TTL: Time to Live, 8 bits
Label
Exp.
S
TTL
Layer 2 Header
(eg. PPP, Ether,
ATM, Frame Relay)
•••
Network Layer Header
and Packet (eg. IP)
4 Octets
MPLS Label Stack
1
n
Label Stack
Entry Format
Labels are identifiers used in forwarding
Label values have meaning between two nodes NOT end-to-end
There may be multiple labels stacked per packet
Format:

## Slide 15: MPLS Basics
MPLS Domains
MPLS Nodes and Label Switch Routers
Label Switch Path
Label Edge Routers
  Ingress, egress and transit nodes
MPLS Domain
Label Switch Router
Label Switch Path
Ingress
Egress
Transit

## Slide 16: MPLS Operation
1a. Routing protocols (e.g. OSPF-TE, IS-IS-TE) exchange reachability to destination networks
1b. Label Distribution Protocol (LDP)
establishes label mappings to destination network
2. Ingress LER receives packet and “label”s packets
IP
IP
10
3. LSR forwards packets using label swapping
IP
20
IP
40
4. LER at egress removes label and delivers packet
IP

## Slide 17: MPLS Operation
Packets are switched, not routed, based on labels
Labels are filled in the packet header
Basic operation:
  Ingress LER (Label Edge Router) pushes a label in front of the IP header
  LSR (Label Switch Router) does label swapping
  Egress LER removes the label (POP)
The key : to operation of MPLS
  Link state routing protocols
    Exchange network topology information for path selection
    OSPF-TE, IS-IS-TE
  Signaling/Label distribution protocols:
    Set up LSPs (Label Switched Path)
    LDP, RSVP-TE, CR-LDP

## Slide 18: MPLS Routing
To compute LSP, LSRs collect network topology and resource information about each link
Paths are computed to avoid links that cannot support the service level of an LSP (e.g. link with insufficient bandwidth)
OSPF-TE and ISIS-TE Extensions
  Provides information for path selection
    Aka Shortest Path first - SFP/ Constrained Shortest Path First - CSFP
  carry information related to link attributes/states, to be used for explicit route calculation (e.g. available/reserved bandwidth)
  Is used for finding/calculating TE path
  Traffic engineering metric
    Maximum bandwidth
    Maximum reservable bandwidth
    Unreserved bandwidth
    Administrative group
      Also called Resource Class/Color
Notes: Open shortest path first

## Slide 19: MPLS signaling
To use an LSP, it must be signaled across your routers.
  An LSP is a network-wide tunnel, but a label is only a link-local value.
An MPLS signaling protocol maps LSPs to specific label values.
  There are two main MPLS routing protocols in use today:
    Label Distribution Protocol(“LDP”) : A simple non-constrained (doesn’t support traffic engineering) protocol.
    Resource Reservation Protocol with Traffic Engineering (“RSVP-TE”) : A more complex protocol, with more overhead, but which also includes support for traffic-engineering via network resource reservations.

## Slide 20: Signaling: LDP (Label Distribution Protocol) Operation
Peer Discovery
Transport connection establishment
Session initialization
Label exchange
Session maintenance
Hop-by-Hop operation

## Slide 21: Signaling: LDP Operation
Ingress LSR send Label Request Messages to Egress LSR to setup LSP
  Includes one or more hosts/prefixes
Routes
192.233.197.0/24
209.80.0.0/18 63.74.77.0/24
198.254.24.0/23
Routes
63.74.77.0/24
198.254.24.0/23
Routes Labels
192.233.197.0/24 28
209.80.0.0/18 28 63.74.77.0/24 65
198.254.24.0/23 65
Routes Labels
63.74.77.0/24 92
198.254.24.0/23 92
Egress LSR send Label Mapping Messages
Request and Reply messages follow paths that are limited to IP shortest path routes
LSP are along shortest paths

## Slide 22: Interesting MPLS aspects
Separation of control and Data plane
packet forwarding in each router decoupled from label switching and LSP taken up and down in the network
Independent network control mechanisms
LSP set up and down based on different criteria using different protocols
2. Packet forwarding processing
LSR can process more packets
Label switching and forwarding is simpler and performed in hardware

## Slide 23: Interesting MPLS aspects
Connection Oriented:
  IP packets are forwarded based on the destination address same address means same link
  MPLS connection is oriented: Packets are organized in packet streams called forward equivalent classes (FEC)
  Packets with different service requirements are grouped in different FEC
  Each FEC has an LSP
  Allows Traffic Engineering (TE) (load balancing, avoid congestion)
  MPLS allows multiple VPN over single IP network
Explicit Routing
  IP routing follows shortest path
  MPLS allows explicit routing: LSP can be chosen to offer certain QoS assurances (e.g links with sufficient reserved bandwidth)

## Slide 24: MPLS tunnelling and label stacking

## Slide 25: Lambda as a Label in MPLS (MPλS)
Multiprotocol Lambda Switching (MPλS) is the optical analogy of MPLS.
Wavelength is the new label
Labels in MPLS can be viewed as analogous to optical channels in optical networks.
LSRs are viewed as analogous to OXCs.
The data plane of an LSR uses the label-swapping paradigm to transfer a labelled packet from an input port to an output port.
The data plane of an OXC uses a switching matrix to connect an optical channel (OCh) trail from an input port to an output port.

## Slide 26: Lambda as a Label in MPLS (MPλS)
Channel arrives on Port 1 on 2, the "green" lambda
Connection table indicates that this channel should be space-switched to Port 4
At Port 4, 2 is available for onward transmission
Connection Table
In
(port,Lambda)
Out
(port, Lambda)
(1, 2)
(1, 3)
(1, 1)
(2, 1)
(4, 2)
(4, 3)
(4, 2)
(3, 1)
2
2
Port 1
Port 2
Port 3
Port 4
Case 1a: No wavelength translation

## Slide 27: Lambda as a Label in MPLS (MPλS)
Channel arrives on Port 1 on 3, the “grey" lambda
Connection table indicates that this channel should be space-switched to Port 4
At Port 4, 3 is available for onward transmission
Connection Table
In
(port,Lambda)
Out
(port, Lambda)
(1, 2)
(1, 3)
(2, 3)
(2, 1)
(4, 2)
(4, 3)
(4, 1)
(3, 1)
3
Port 1
Port 2
Port 3
Port 4
Case 1b: No wavelength translation
3

## Slide 28: Lambda as a Label in MPLS (MPλS)
Channel arrives on Port 2 on 3, the “grey" lambda
Connection table indicates that this channel should be space-switched to Port 4
At Port 4, 3 is already in use, so lambda is translated to 1, the "red" lambda
Connection Table
In
(port,Lambda)
Out
(port, Lambda)
(1, 2)
(1, 3)
(2, 3)
(2, 1)
(4, 2)
(4, 3)
(4, 1)
(3, 1)
3
1
Port 1
Port 2
Port 3
Port 4
Case 2: Wavelength translation

## Slide 29: Generalized MPLS(GMPLS)
Very active area within the IETF - Generalized MPLS (GMPLS)
Developed from MPLS
generalize the concept of a “label”
A previous version is “Multi-Protocol Lambda Switching”
Extend the MPLS to support more interfaces other than packet switch
  Packet Switch Capable (PSC)
    Router/ATM Switch/Frame Reply Switch
  Time Division Multiplexing Capable (TDMC)
    SONET/SDH ADM/Digital Cross connects
  Lambda Switch Capable (LSC)
    All Optical ADM or Optical Cross connects (OXC)
  Fiber-Switch Capable (FSC)
  LSPs of different interfaces can be nested inside another
  consistent path establishment across variety of technologies

## Slide 30: GMPLS Controlled Lightpath
  Request propagated to egress
  Egress responds with lambda
  Response propagated upstream to ingress
Data flow
λ2
λ2
λ5
λ2
λ8
Reuse of MPLS and IP Control
  Ingress initiates lightpath setup

## Slide 31: Packet and Cell Switching
MPLS
“label” == shim header
if0
if100
if101
if1
pkt0
pkt2
pkt0
pkt2
pkt0
pkt2
pkt0
pkt2

## Slide 32: TDM (SONET/SDH) Switching
l1
l100
l1
l100
t0
t2
t0
t2
t0
t2
t0
t2
TDM
“label” == TDM time slot

## Slide 33: Lambda Switching
l
lp - l1
l100
l1
l100
l100
{l..l}1
{l..l}10
{l..l}1
{l..l}10
OEO
“label” == lambda frequency
OOO

## Slide 34: Port Switching
Fiber #1
Fiber #N
Fiber #1
Fiber #N
Fiber #1
Fiber #1
Fiber #1
Fiber #N
Fiber #1
Fiber #N
“label” == fiber port

## Slide 35: Generalized MPLS
GMPLS is a superset of MPLS and MPS
  Apply MPLS control plane techniques to optical switches and IP routing algorithms to manage lightpaths in an optical network
Data Plane
MPLS, SONET/SDH, s/WDM, Ports
GMPLS Control Plane
RSVP-TE, CR-LDP OSPF, IS-IS
GMPLS made some modifications on MPLS
  Separation of signaling and data channel
  Support more types of control interface
  Other enhancement

## Slide 36: Generalized Labels
MPLS labels are a simple 32 bit quantities
Extend the MPLS to support more interfaces other than packet switch
  Packet Switch Capable (PSC)
    Router/ATM Switch/Frame Reply Switch
  Time Division Multiplexing Capable (TDMC)
    SONET/SDH ADM/Digital Crossconnects
  Lambda Switch Capable (LSC)
    All Optical ADM or Optical Crossconnects (OXC)
  Fiber-Switch Capable (FSC)
LSPs of different interfaces can be nested inside another
Natural hierarchy is established
FSC
LSC
LSC
TDMC
TDMC
PSC

## Slide 37: Switching Hierarchy

## Slide 38: Hierarchical LSP

## Slide 39: GMPLS LSP formation
A Path request (Path 1) is generated at R0 that is sent to R1.
At node R1 (a boundary node) this arrival triggers a requirement for a new LSP (LSP2) from R1 to R9.
These dynamic LSP creation requests are triggered until Path 4 is generated at O3.
Following successful establishment of LSP4, the Path 3 message is tunneled through LSP4.
a lower-level LSP creation request being tunneled through the higher-level LSP so formed, continues until the initial LSP (LSP1) is successfully created, thus forming a hierarchy.

## Slide 40: GMPLS and MPLS Differences (Routing Extension)
Extensions to routing (Mainly OSFP) to support
    Routing and wavelength/time slot assignment
    Interface Switching Capability
      Identifies type of switching supported and Maximum LSP bandwidth per priority

## Slide 41: End of session 9
Part 1

## Slide 42: Optical Networks [EENGM0003]
Dr. George T. Kanellos
[gt.kanellos@bristol.ac.uk]

## Slide 43: Link Management
Need to manage and maintain the health of the control and data planes between neighboring nodes:
Need to address a common set of issues
  Isolation of faults transparent networks
  Scale the number of links without increasing configuration
  Handle case where transmission (e.g., WDM) and switching are separated = very large number of component / per-lambda links
New protocol needed to resolve these issues, e.g. LMP (Link Management Protocol)

## Slide 44: LMP - Link Management Protocol
Control Channel Management
  Negotiate link parameters (keep-alive messages) and ensure health of a link (hello protocol)
Link Property Correlation
  Discover and agree data link properties of adjancent nodes
Link Verification
  Map interface IDs and verify data connectivity (PING-like test message)
Fault Management
  Detect and isolate faults

## Slide 45: Network Management functions
Performance Management
Monitor and Measure the performance of the network (QoS)
Fault management
is the function responsible for detecting failures when they happen and isolating the failed component.
Conﬁguration management
Resource management (managing the equipment, routing)
connection management (setting up, taking down, and keeping track of connections)
adaptation management: convert external client signals into appropriate signals inside the optical layer.
Security management
administrative functions such as authenticating users and setting attributes such as read and write permissions on a per-user basis.

## Slide 46: Layered Network Management
Multiple layers of management
  Management functionality in each network element and support on each communications link
  Element management system (EMS): Manages a subnetwork of the network elements
  Network management system (NMS): talks to the EMSs to get the overall view of the network.

## Slide 47
Optical Network Management
Management Plane
OTN
Transport Plane
Control
Plane
(Embedded Controller)
  Control plane is positioned between transport and management planes.
  NEs are controlled either by control plane or by both management plane and CP.
  Management plane, configures and supervises the Control plane .
    Routing constraints, policy
    Performance monitoring
  Management plane has ultimate control over all transport plane and control plane entities.
  Management plane is also manage/control inter domain networking and connection establishment
Notes: This slide shows the distribution of the support to four types of CP interfaces. These are the I-NNI for intra-domain, E-NNI for inter-doamin CP, the network side of UNI and client side of UNI. Team C supports full peer model and needs only to implement I-NNI interface. Team B shows a uniform support of all four CP interface types. This will provide a rich set of interoperability test scenarios.

## Slide 48: Optical Network Management

## Slide 49: Optical Network Optimization (WDM Network)
Optimization Objective
  Route all the lightpaths using the minimum number of wavelengths
  Route all the lightpaths using the minimum number of fibers
  Route all the lightpaths minimizing the total network cost, taking into account also switching systems
This can be achieved by appropriate Routing and Wavelength Assignment (RWA) algorithms
  Offline
    For all light paths in advance
    Requires knowledge of all connectivity request in advance
  Online
    For light path connectivity demands coming during operation

## Slide 50: Routing and Wavelength Assignment (RWA)
Input parameters:
  a set of lightpaths that need to be established in the network
  physical topology
  number of fibers and number of wavelengths on fiber
  constraints: e.g., wavelength continuity, physical impairments, survivability, etc
Objective :
  Find the routes over which these lightpaths should be set up
  the wavelengths which should be assigned to these lightpaths meet all constraints
  Lightpath is blocked when it can not be setup due to lack of resources (routes and/or wavelengths) or due to other constraints
  The corresponding network optimization problem is to minimize the blocking probability

## Slide 51: RWA Constrains
Wavelength continuity
  Wavelength continuity constraint can be alleviated by wavelength converter functionality at all or some selected nodes
  No wavelength conversion functionality in the network lightpaths operate on the same wavelength across all fiber links
  Lightpath may switch between different wavelengths on its route from its origin to its termination
  Tradeoff: cost vs. performance
Physical Constraints
  Directly related to the nature of the optical physical medium and transparent transmission
  Optical signal impairments affect the quality of the lightpaths Limiting reach of the lightpaths
  Physical impairments can be mitigated by signal regeneration
  3R regeneration: Re-amplification, Re-shaping and Re- timing
  Tradeoff: cost vs. performance

## Slide 52: RWA Methods
Integer Linear Programming (ILP) formulation
  Mathematically optimized routing model
  Heuristically optimized routing methods
Routing methods
  Shortest Path
    selects the shortest source- destination path (# of links/nodes)
  Least Loaded Routing
    avoids the busiest links
  Least Loaded Node
    avoids the busiest nodes

## Slide 53: Network Survivability
Network Survivability Definition: The process of transferring client service on to spare network capacity in the event of failure in the network
One of the most important assets of future all-optical networks will be survivability. The enhancement of the transport network survivability can be achieved through use of different strategies. The two main approaches are protection and restoration
Protection uses a pre-assigned capacity between nodes in order to replace the failed or degraded transport entities
Restoration can use any capacity available between nodes in order to find a transport entity that can replace the failed one. Restoration is based on re-routing algorithms to find a new path to recover failed network entities, at the time the failure occurs

## Slide 54: Protection & Restoration
Compared to protection techniques, restoration is more flexible and generally makes a much more efficient use of the network capacity.
Restoration takes a longer time to restore the traffic affected by the failure, due to the need to find a new route in the network.
In general:
  automatic protection can be applied to network architectures as point to point, rings and meshed networks
  restoration is usually applied to meshed networks with cross-connect equipment.

## Slide 55: Restoration Process
The main steps of the restoration process can be summarised as follow:
  Detection of the failure
    the failure is detected by the Network Elements and the defect is notified to the Restoration Control Unit (a Network Manager OS, for instance)
  Propagation of control messages
    the control information is propagated between Network Elements and/or Control Units (if required)
  Selection of the new route
    based on the spare resource available in the network, an alternative route for each affected demand is selected.
  Re-routing
    the demands are re-routed by a re-configuration of cross-connects.
  Return to normal
    generally, after fault recovery, the network returns to the initial state, either automatically or manually.

## Slide 56: Restoration Techniques Control Architecture
Centralised control architecture
  The restoration process is operated from a Central Control Unit (CCU) that gets all the information concerning the status of the network, via control communication links and databases
  The databases can be either centralised or distributed
  The CCU may be integrated to the OS, combining capacity planning with restoration
  No communication is required between cross-connects, allowing a great compatibility in terms of equipment
Distributed control architecture
  The restoration process is operated by a number of Control Units located in each Network Element (NE). Each NE then reacts according to a set of rules to a local alarm or a message from an adjacent NE
  The information about the status of the network is distributed between a large number of databases located in the NEs together with CUs
  Each NE maintains in its database only local network information (connections to neighbouring nodes and paths, for instance)
  The NE does not have a global network view and the restoration process requires the exchange of many control messages between NEs, according to a simple set of rules

## Slide 57: Restoration Techniques Control Architecture
Differences between centralised and distributed restoration:
  Distributed control offers restoration times around 2 seconds. For centralised control architecture restoration times are within 20-40 seconds
  With a centralised controllers it is easier to monitor the network configuration than with distributed controllers. This makes it also easier the return to normal
  A scheme with centralised control does not require communication between cross-connects and therefore concerns about vendor dependence are minimised

## Slide 58: End of session 9