## Slide 1: The Transport Layer
Congestion Control

## Slide 2: Principles of congestion control
congestion:
informally: “too many sources sending too much data too fast for network to handle”
different from flow control!
manifestations:
  lost packets (buffer overflow at routers)
  long delays (queueing in router buffers)
a top-10 problem!

## Slide 3: Causes/costs of congestion: scenario 1
two senders, two receivers
one router, infinite buffers
output link capacity: R
no retransmission
maximum per-connection throughput: R/2
unlimited shared output link buffers
Host A
original data: lin
Host B
throughput: lout
R/2
R/2
lout
lin
R/2
delay
lin
large delays as arrival rate, lin, approaches capacity

## Slide 4: Causes/costs of congestion: scenario 2
one router, finite buffers
sender retransmission of timed-out packet
  application-layer input = application-layer output: lin = lout
  transport-layer input includes retransmissions : lin lin
finite shared output link buffers
Host A
lin : original data
Host B
lout
l'in: original data, plus retransmitted data
‘

## Slide 5: Causes/costs of congestion: scenario 2
A
lin
lout
l'in
copy
free buffer space!
timeout
R/2
R/2
lin
lout
when sending at R/2, some packets are retransmissions including duplicated that are delivered!
Host B
Realistic: duplicates
packets can be lost, dropped at router due to full buffers
sender times out prematurely, sending two copies, both of which are delivered

## Slide 6: Causes/costs of congestion: scenario 2
R/2
lout
when sending at R/2, some packets are retransmissions including duplicated that are delivered!
“costs” of congestion:
more work (retrans) for given “goodput”
unneeded retransmissions: link carries multiple copies of pkt
  decreasing goodput
R/2
lin
Realistic: duplicates
packets can be lost, dropped at router due to full buffers
sender times out prematurely, sending two copies, both of which are delivered

## Slide 7: Causes/costs of congestion: scenario 3
four senders
multihop paths
timeout/retransmit
Q: what happens as lin and lin’ increase ?
finite shared output link buffers
Host A
lout
Host B
Host C
Host D
lin : original data
l'in: original data, plus retransmitted data
A: as red lin’ increases, all arriving blue pkts at upper queue are dropped, blue throughput g 0

## Slide 8: Causes/costs of congestion: scenario 3
another “cost” of congestion:
when packet dropped, any “upstream transmission capacity used for that packet was wasted!
C/2
C/2
lout
lin’

## Slide 9: Approaches towards congestion control
two broad approaches towards congestion control:
end-end congestion control:
no explicit feedback from network
congestion inferred from end-system observed loss, delay
approach taken by TCP
network-assisted congestion control:
routers provide feedback to end systems
  single bit indicating congestion (SNA, DECbit, TCP/IP ECN, ATM)
  explicit rate for sender to send at