## Slide 1: Selected Topics on IoT Networking
The IEEE 802.15.4 Standard

## Slide 2: IEEE 802.15.4 PHY
Extremely low-power radio
250Kbps
2.4GHz band, 16 channels (numbered 11…26)
The IEEE 802.15.4g amendment adds:
Frequency bands (e.g. for Sub-GHz operation)
Bitrates
Channel configurations
Modulation options
PHY header options

## Slide 3: 802.15.4 MAC
Connectionless, with ACKs for reliability
Distributed operation (coordinated also specified but not widely used)
CRC-16 for error detection (also CRC-32 in .15.4g)
Low-power operation:
TSCH: Time Slotted Channel Hopping More on TSCH later.

## Slide 4: PHY/MAC Frame Format
MAC addresses are 8-bytes here
  Formally called EUI-64
FCS: A CRC16 (or 32) for error detection
Max length: 127 bytes

## Slide 5: The FCF
The Frame Control Field (FCF) contains information about the rest of the frame:
Frame version (0, 1 or 2) Slight differences in frame format across versions
Frame type: Beacon, Data, ACK, …
AR: Is the sender expecting an ACK?
Describes the format of the Addressing fields (Remember, variable length 0-20 bytes)

## Slide 6: Addressing Fields
Variable length. Contains 4 sub-fields
Destination PAN ID: 0 or 2 bytes
Destination Address: 0, 2 or 8 bytes
Source PAN ID: 0 or 2 bytes
Source Address: 0, 2 or 8 bytes

## Slide 7: MAC addresses in .15.4 (EUI-64)
Similar to classic (e.g. ethernet or WiFi) MAC addresses, but 8-bytes long.
Example: 00:12:4b:00:18:75:69:a5
ff:ff:ff:ff:ff:ff:ff:ff
Text representation: 8 pairs of hex characters, separated by a “:”
You may also see it written as: 0012.4b00.1875.69a5
All 1s is the broadcast address. Often used in short (2-byte) mode (ff:ff) in the .15.4 MAC layer header’s destination address field

## Slide 8: EUI-64
An EUI-64 address can be:
Universally Administered Addresses (UAA) Hard-coded on hardware at the factory
00:12:4b:00:18:75:69:a5
Organization Unique Identifier (OUI) Identifies the manufacturer
Locally Administered Addresses (LAA) Administrator override of the UAA
Assigned by the manufacturer

## Slide 9: The Universal/Local (U/L) bit
It is possible to distinguish between UAA and LAA by looking at the Universal/Local (U/L) bit
00:12:4b:00:18:75:69:a5
00000000 (binary)
The U/L bit (2nd least significant bit of the MSB)
0: The address is a UAA
1: The address is an LAA