## Slide 1: Selected Topics on IoT Networking
Low-Power Operation

## Slide 2: Low-Energy Operation
x1000

## Slide 3: Radio Duty-Cycling
IoT Devices save energy by sleeping (turning off their radio and cpu)
  E.g. 10% radio duty cycle == radio is activated 10% of the time
The challenge
  For two devices to communicate, they both need to be awake at the same time
  Question: How do they coordinate?

## Slide 4: Answer: Asynchronous
Sender-Initiated
  Sender transmits packets repeatedly until receiver responds back
  Receiver periodically wakes up to check for incoming packets
Receiver-Initiated
  Receiver transmits beacons periodically to signal its availability
  Sender listens for beacons and transmits the packet after them
Energy wasted for additional radio usage (overhead)
  Idle listening, unreceived transmissions

## Slide 5: Different answer: Synchronous
Schedule rendezvous points when both sender and receiver wake up
Requires Time Synchronisation
Some level of de-synchronisation can be addressed with a guard time
  Yet, guard time increases the radio duty-cycle (idle listening)
Rendezvous point
Guard Time
Wake-up Point
Sleep Point
How do IoT devices measure time?

## Slide 6: Time Synchronisation
IoT Devices measure time using some h/w clock source
Hardware clocks fed by oscillators. Typically crystal or RC
  Generates an electrical signal at a (hopefully) precise frequency
  A typical frequency is 32768 Hz
Challenge: Oscillators can be somewhat inaccurate
  As a result, h/w clock sources will drift apart
  Drift is measured in ppm (parts per million)
  1 ppm drift means a de-synch of:
    1usec / 1sec or
    1 ms every 1000 sec (16.6 minutes!)

## Slide 7: Time Synchronisation
Sources of clock drift
  Production spread (+/- 20 ppm)
  Temperature difference (40 ppm @ 30 degrees difference)
  Measurement error (e.g. quantisation error)
Quantization error example:
  With a 32768 Hz crystal, each pulse is ~30.51 usec
  327 ticks: ~9979 usec
  328 ticks: ~10009 usec
  Impossible to measure 10ms precisely!
What’s even worse: Two theoretically identical oscillators may behave somewhat differently