## Slide 1: Selected Topics on IoT Networking
Time-Slotted Communications

## Slide 2: Time-Slotted Communication
Time synchronisation enables time-slotted communication
  Time is quantised in time slots, e.g. 10 ms
  Communication is based on a repeating schedule
The schedule controls performance
  Energy Consumption, e.g. 1/7 = 14% duty cycle
  Throughput, e.g. up to 100/7 = 14 frames per sec
  Delay, e.g. up to 7 x 10 ms = 70 ms
1 | 2 | 3 | 4 | 5 | 6 | 7
A→B |  |  |  |  |  | 

## Slide 3: Contention or Dedicated?
Contention-based
Consider a third device
Dedicated Slots
1 | 2 | 3 | 4 | 5 | 6 | 7
A→B |  |  |  |  |  | 
A
C
B
1 | 2 | 3 | 4 | 5 | 6 | 7
 | C→B |  |  |  |  | 
1 | 2 | 3 | 4 | 5 | 6 | 7
A→B |  |  |  |  |  | 
1 | 2 | 3 | 4 | 5 | 6 | 7
C→B |  |  |  |  |  | 
A’s schedule
C’s schedule
A’s schedule
C’s schedule

## Slide 4: Wireless Channels
Let’s assume that we have 2 channels
The channel can be a second dimension to my schedule
A
C
B
D
 | 1 | 2 | 3 | 4 | 5 | 6 | 7
Ch 1 | A→B |  |  |  |  |  | 
Ch 2 |  |  |  |  |  |  | 
A’s schedule
 | 1 | 2 | 3 | 4 | 5 | 6 | 7
Ch 1 |  |  |  |  |  |  | 
Ch 2 | C→D |  |  |  |  |  | 
C’s schedule

## Slide 5: Channel Hopping
What if a channel in the schedule is a lot busier than another one?
Channel Hopping (or Frequency Hopping)
  Transmitter and receiver change channels in a pseudo-random pre-agreed pattern
1 | 2 | 3 | 4 | 5 | 6 | 7 | 1 | 2 | ...
A→B |  |  |  |  |  |  | A→B |  | 
11 | 26 | 16 | 11 | 26 | 16 | 11 | 26 | 16 | 11
11 | 26 | 16
Hopping Sequence (or pattern)

## Slide 6: Time-Slotted, Channel Hopping (TSCH)
Part of the IEEE 802.15.4 spec
  Synchronous MAC protocol (global synchronisation)
  Communication is based on a repeating schedule
  Channel is based on a repeating hopping sequence
D. Dujovne, T. Watteyne, X. Vilajosana and P. Thubert, "6TiSCH: deterministic IP-enabled industrial internet (of things)," in IEEE Communications Magazine, vol. 52, no. 12, pp. 36-41, December 2014.

## Slide 7: IEEE 802.15.4 TSCH
Advantages
  Very reliable - Up to 99.999% PDR reported
  Very predictable energy-consumption
Disadvantages
  Expensive to join the network
  Not great when nodes are mobile
  Time-synchronisation challenges (as discussed) remain
  Complex implementation
Related standards and other active research
  6tisch: 6LoWPAN over TSCH
  How schedules are created and distributed
    Static, centralised, distributed
  How hopping sequences are created and distributed