## Slide 1: Selected Topics on IoT Networking
6LoWPAN: IPv6 over Low-power, Wireless Personal Area Networks (WPANs)

## Slide 2: Constrained Network
RFC 4919 | IPv6 over Low-Power Wireless Personal Area Networks (6LoWPANs) Overview, Assumptions, Problem Statement, and Goals | Aug. 2007
RFC 4944 | Transmission of IPv6 Packets over IEEE 802.15.4 Networks | Sep. 2007
RFC 6282 | Compression Format for IPv6 Datagrams over IEEE 802.15.4-Based Networks | Sep. 2011
Radio: IEEE 802.15.4
  very small data packets
  low power RF transceivers (thus, low range)
How do we transport TCP/IP datagrams over this medium?

## Slide 3: IPv6 over 802.15.4
MAC
3 – 23
127 bytes max frame size
2
FCS
102-122 bytes

## Slide 4: IPv6 over 802.15.4
IPv6
UDP
40
8
Simple UDP message
56% overhead…
MAC
21
2
FCS
54 Bytes of User Data

## Slide 5: 6LoWPAN Functions
Fundamentally, 6LoWPAN does two things:
Header compression
Fragmentation and Re-assembly
Source: “Internet Protocol, Version 6 (IPv6) Specification”, IETF RFC 2460
https://tools.ietf.org/html/rfc2460

## Slide 6: 6LoWPAN Compression
6LoWPAN
MAC
21
2
FCS
up to 100
2+
Simple UDP message using the 6LoWPAN adaptation layer
≈ 20% best-case overhead…
Realistic: ≈ 25 bytes of overhead