## Slide 1: Net Sys & Apps
Week 19

## Slide 2: IEEE 802.15.4
Q: What is the default bitrate of IEEE 802.15.4 when operating at the 2.4GHz band?
A:250kbps

## Slide 3: IEEE 802.15.4
Q: What is the default bitrate of IEEE 802.15.4 when operating at the 2.4GHz band?
A:250kbps
Q: How much time does it take to transmit 1 byte?
A:32us

## Slide 4: IEEE 802.15.4
Q: What is the default bitrate of IEEE 802.15.4 when operating at the 2.4GHz band?
A:250kbps
Q: How much time does it take to transmit 1 byte?
A:32us
Q: How much time does it take to transmit a frame of maximum size?
  A:127*32us = 4.064 ms

## Slide 5: Energy Calculations
MCU State | Current |  | RF State | Current
MCU Active (Running @48MHz) | 3mA |  | RF RX | 6mA
MCU Sleeping (Paused) | 0.5mA |  | RF TX - 5-dBm output power | 9mA
MCU Off | 3μA |  | RF Off | 0uA
Assume a System-on-Chip (SoC) with an integrated MCU and RF transceiver and the power consumption characteristics shown in the table

## Slide 6: Energy Calculations
Q: How much charge is consumed to transmit 125 bytes? (MCU is Sleeping while the RF is TXing)
A: Q = I*t
I = (0.5+9)m *4ms = 38 uC
MCU State | Current |  | RF State | Current
MCU Active (Running @48MHz) | 3mA |  | RF RX | 6mA
MCU Sleeping (Paused) | 0.5mA |  | RF TX - 5-dBm output power | 9mA
MCU Off | 3μA |  | RF Off | 0uA

## Slide 7: Energy Calculations
Q: How much charge is consumed to transmit 125 bytes? (MCU is Sleeping while the RF is TXing)
A:
Q = I*t
I = (0.5+9)m *4ms = 38 uC
Q: And how much energy is consumed? (Assume a supply voltage of 3V)
A: E=qv=38uC*3V =114uJ
MCU State | Current |  | RF State | Current
MCU Active (Running @48MHz) | 3mA |  | RF RX | 6mA
MCU Sleeping (Paused) | 0.5mA |  | RF TX - 5-dBm output power | 9mA
MCU Off | 3μA |  | RF Off | 0uA

## Slide 8: TSCH
TSCH Timeslot / Total Timeslot Duration = 10ms |  |  |  |  |  |  |  | 
Transmitter |  |  |  |  |  |  |  | 
 | Guard Time | Guard Time |  | TX Frame | Wait | RF On | RX ACK | Rest of Timeslot
 |  |  |  | 125 Bytes |  |  | 5 Bytes | 
 |  | Guard | RF On | RF RX Frame | Wait |  | TX ACK | Rest of Timeslot
Receiver |  |  |  |  |  |  |  | 
Timeslot Start – Slight Clock De-Synch
Waits for Transmitter to TX
Waits for ACK

## Slide 9: TSCH
TSCH Timeslot – Transmitter / Total Timeslot Duration = 10ms | TSCH Timeslot – Transmitter |  |  |  | 
 | Guard Time | TX Frame | Wait for ACK | RX ACK | Rest of Timeslot
 |  | 125 Bytes |  | 5 Bytes | 
Time | 2ms | 4ms | 840μS | 160ms | 3ms

## Slide 10: TSCH
TSCH Timeslot – Transmitter / Total Timeslot Duration = 10ms | TSCH Timeslot – Transmitter |  |  |  | 
 | Guard Time | TX Frame | Wait for ACK | RX ACK | Rest of Timeslot
 |  | 125 Bytes |  | 5 Bytes | 
Time | 2ms | 4ms | 840μS | 160ms | 3ms
RF State | Off | TX | RX | RX | Off
RF Charge | 0C | 36C | 6uc | ??? | 0
MCU State | Off | Sleep | Active | Active | Off
MCU Charge | 6nC | 2uC | 3uc | ??? | 9nC
Total Charge | 6nC | 38uC | 9uC | ??? | 9nC
MCU State | Current |  | RF State | Current
MCU Active (Running @48MHz) | 3mA |  | RF RX | 6mA
MCU Sleeping (Paused) | 0.5mA |  | RF TX - 5-dBm output power | 9mA
MCU Off | 3μA |  | RF Off | 0uA