## Slide 1
Diversity
Notes: 1

## Slide 2: Diversity (1)
Extreme and rapid signal variations are associated with mobile radio reception
Diversity
  reduces these fluctuations (reduces the effects of fading) into a more acceptable range
  we have two or more transmission paths that suffer different fading statistics, carrying the same message
    i.e. independent/uncorrelated transmission paths
Two or more independent/uncorrelated transmission paths give us the opportunity to select one of them or combine them so we reduce the impact of fast fading.
(1,0)
(0,0)

## Slide 3: Diversity (2)
Why effects of fading are reduced?
  It is highly improbable that both uncorrelated signals will enter a fade at the same time
(1,0)
(0,0)
If the branches are highly uncorrelated, usually when one enters a signal fade, the other one will most probably have a strong signal
If we monitor the signal strength at the branches, the distortion that results, could be minimised with signal processing

## Slide 4: How can we generate those uncorrelated paths???
Space Diversity
Angle Diversity
Time Diversity
Frequency Diversity

## Slide 5: Space Diversity
Also known as Antenna diversity
The transmitted signal is received via a number of different antennas
Antennas are spaced sufficiently far apart to ensure independent and uncorrelated fading
Simple form of diversity, no additional spectrum required
  Many applications

## Slide 6: Space Diversity (1)
Transmitter Space diversity
  Transmit power is split across the M antennas
Receiver Space diversity

## Slide 7: Space Diversity (2)
  Antenna spacings are usually a fraction of the wavelength
  It is common to use or
    Microscopic diversity
Receiving antennas should be set such that the signals on adjacent branches are uncorrelated
  Antennas spaced at a distance greater than the coherence distance
  Exploits small scale fading, characterised by deep and rapid amplitude fluctuations as the mobile moves a distance of a few wavelengths

## Slide 8: Space Diversity (3)
Various antenna spacings have been tried
  For a handset, has been accepted as the value that offers the best compromise between size of antenna array and system performance.
Optimum spacing depends on the azimuth angle spread of multipaths, which influences the Doppler spread
The angle spread depends on the specific environment
Factors affecting the choice of antenna spacing:
  Determined by the spaced-distance correlation function
    Function of the multipath power and the angle spread
The narrower the angle spread, the wider the required spacing
  due to the similar type of multipaths (eg. Reflection from one wall)

## Slide 9: Space Diversity (4)
No increase in transmitted power and bandwidth required
Coherent combining of the uncorrelated signals, results in an increase in the received SNR
If antennas are mounted at a roof height
  The majority of energy is arriving from the location of the terminal (specific direction)
    Thus the angle and doppler spread are low, and the required spacing needs to be larger (2-3 wavelengths)

## Slide 10: Space Diversity – Macroscopic Diversity
Choose a basestation, which is not shadowed, to have the best SNR at the forwarded link
Exploits large scale fading caused by shadowing
  Due to variations in the terrain profile and nature of the surroundings

## Slide 11: Space Diversity Trial (1)
Indoors and Outdoors (MVB) mmWave (at 60GHz) modem measurements (5G-Xhaul)
  Received SNR, Data Rate and Average Packet Delivery rate for different locations and several modulation and coding schemes

## Slide 12: Space Diversity Trial (2)
Indoors and Outdoors (MVB) mmWave (at 60GHz) modem measurements
  16cm and 52cm indoors
  40cm and 80cm outdoors

## Slide 13: Angle (Pattern) Diversity (1)
Signals arriving from different directions are uncorrelated
So, directive antennas can be used to produce the required independently faded diversity signals
Directive antennas restrict angles over which rays may be received
  so the effects of Doppler spread and time delay spread are reduced

## Slide 14: Time Diversity (1)
System operates by retransmitting the message signal after a suitable time delay
Copies of the signal are transmitted over different time periods
Delay should be greater than the coherence time of the channel
  Remember in space diversity the antenna spacing should be greater than coherence distance
Transmitted signal: s(t)

## Slide 15: Time Diversity (2)
This method:
  Reduces the efficiency
  Requires information storage at both ends, introducing delay
    unacceptable for audio
No improvement if the user is static, although a slight gain can be achieved due to the time-variability associated with other motion in the channel

## Slide 16: Frequency Diversity (1)
The required signal is transmitted on more than one frequencies
Copies of the signal modulated in different frequencies
Only one antenna is required
Transmitted signal: s(t)
Transmit power is split among the carriers

## Slide 17: Frequency Diversity (2)
There is no delay
This method requires extra signal bandwidth, so it is not desirable!
Frequency separation should be enough
to ensure uncorrelated fading, i.e. greater than coherence bandwidth

## Slide 18: Diversity Combining Strategies
Uncorrelated paths can be combined to improve the resulting signal to noise statistics
In ascending order of complexity, cost and performance, the strategies are:
  Switched (Scanning) Diversity
  Selection Diversity
  Equal Gain Combining
  Maximal Ratio Combining
(1,0)
(0,0)

## Slide 19: Switched (Scanning) Diversity
Cheap
Simple
  requires one circuit to measure the average signal power to perform Received Signal Strength Indication (RSSI)
    power at the received signal
The current branch is selected until it fails a given metric. Then, the next branch in turn is blindly selected. If it satisfies the metric, it remains selected, otherwise the system moves on to the next branch

## Slide 20: Switched Diversity – fixed threshold (1)
1. Select branch A
- 40dBm
- 50dBm
- 10dBm
5dBm
-45dBm
2. RSSI: - 10dBm>- 40dBm
3. Again select branch A
4. RSSI: - 50dBm<- 40dBm
5. Select branch B
6. RSSI: 5dBm>- 40dBm
7. Again select branch B
8. RSSI: -45dBm<- 40dBm
9. Switch to branch A
Simple metric based on signal strength

## Slide 21: Selection Diversity (1)
more complex
more expensive
  signal strength on each branch is estimated in parallel
The most appropriate branch or antenna is always chosen from those available
Many techniques to choose a branch, usually the largest RSSI is chosen
Selection combining ensures that the stronger of the available envelopes is always chosen

## Slide 22: Selection Diversity (1)
Parallel scanning
Selection of branch with higher RSSI or SNR

## Slide 23: Selection Diversity (2)
Slightly better fading statistics compared to switched diversity
Still we discard signals coming to non-selected branches!

## Slide 24: Maximal Ratio & Equal Gain Combining
Both techniques are known as linear combiners
  various signal inputs are individually weighted and added
Post-detection combining: if combining takes place after detection
Pre-detection combining: if combining is implemented before detection
  It requires co-phasing to be applied before signals are combined, in order to prevent the possibility of destructive summation

## Slide 25: Maximal Ratio Combining
Each branch is weighted before summation in proportion to its own SNR
The resulting output from the combiner is a weighted, co-phased summation of all the diversity branches available at the RX
It optimises the received SNR at the output from the combiner
It represents the optimal combining strategy
  maximises SNR

## Slide 26: Equal Gain Combining
Simpler approach
Gain of each branch is set to one, and signals are simply co-phased and summed
Sub-optimal strategy, but avoidance of any signal to noise power estimation is highly attractive
Performance is marginally below that for maximal ratio combining
Good compromise among cost, complexity and performance

## Slide 27: Diversity Improvement
Fading statistics with/without use of Selection Diversity (based on RSSI)
3%
0.06%
Probability of fading lower than -15dB on the mean:
- 3% for single branch
- 0.06% for the two branches with selection diversity

## Slide 28: Overall
Switched (Scanning) Diversity - simple and cheap - current branch selected till it falls below threshold - fixed or variable threshold | Selection Diversity - more complex and expensive - scans branches and selects the one with highest RSSI - slightly better than switched diversity
Maximal Ratio Combining - signals are individually weighted and combined - pre-detection: signals co-phased before combining - optimises SNR - optimal technique | Equal Gain Combining - same weight to all signals - same gain (=1) for all signals - less complex than MRC - slightly worse performance compared to MRC