## Slide 1: Optical communications and data networks (EENGM2001)
Siddarth K Joshi

## Slide 2
Multiplexing
Multiplexing:
Wavelength
Time
Spatial mode
Polarisation
Multiplexing: The process of mixing various data streams together into the same optical fibre
Remember the optical interleaver?

## Slide 3
Optical Interleaver: Recap
Combines pulses with different timing into a single output stream
(a type of multiplexing)
Compresses the wavelength bandwidth of both signals to increase the capacity of the channel

## Slide 4
Wavelength multiplexing
Why WDMs?
Types
Standards
Thin film WDMs
Arrayed waveguide gratings
Add drop WDMs
Reconfigurable optical add-drop multiplexer
WDM topologies
Practical examples
Learning outcomes
Explain WDMs in modern networks
Calculate bandwidth and number of channels needed for different topologies

## Slide 5
Wavelength multiplexing
Wavelength: Colour of the light used
Most modern optical communications

## Slide 6
Wavelength multiplexing

## Slide 7
Bi-directional communication also possible.
WDM filters work in both directions
Mux/Demux logical names
Transmitter
Receiver
Wavelength multiplexing

## Slide 8
Traffic grows much faster than new long-distance cables.
Need to increase capacity of each cable!
Wavelength multiplexing

## Slide 9
Coarse WDM
Dense WDM
Wavelength multiplexing

## Slide 10
CWDM | DWDM
Cheaper | More expensive
Lasers not stabilised | Stabilised to stay within bandwidth
≈ 10Gb/s | Up to 1 Tbps
< 80 Km | Ultra long reach
18 channels in O to L bands | 45 channels in C band alone
Wavelength multiplexing

## Slide 11
CWDM | DWDM
Cheaper | More expensive
Lasers not stabilised | Stabilised to stay within bandwidth
≈ 10Gb/s | Up to 1 Tbps
< 80 Km | Ultra long reach
18 channels in O to L bands | 45 channels in C band alone
Wavelength multiplexing
Large channel bandwidth
Fast Modulation
Hard to modulate faster than 40 Gbps

## Slide 12
λ2
λ1
-3 dB
Bandwidth
Δλ = |λ1 – λ2| in terms of wavelength
Δf = |f1 – f2| in terms of frequency
Bandwidth
P
P
Power
Wavelength multiplexing

## Slide 13
Typically filters have a top hat profile not gaussian
Bandwidth defined in the same way
Wavelength multiplexing

## Slide 14
Cross talk
Cross talk: Signal from one multiplexed channel enters into another channel causing an increase in noise.
Wavelength multiplexing

## Slide 15
Large channel bandwidth
More Cross talk
More noise
Shorter link distances
Wavelength multiplexing

## Slide 16
ITU: International Telecommunication Union
Standards specify the central wavelength and Spacing for both CWDM and DWDM
Wavelength multiplexing

## Slide 17
Bandwidth is not the same as spacing
0
-3
-6
-9
-12
-15
Spacing
Bandwidth
Wavelength multiplexing

## Slide 18
ITU grid for CWDM:
Spacing = 20nm
Center wavelengths 1270 nm, 1290 nm, 1310 nm, ... , 1590 nm, 1610 nm
Wavelength multiplexing

## Slide 19
ITU grid for DWDM:
Spacing = 100 GHz ≈ 0.8 nm
Channel number | Central Frequency (THz) | Central wavelength (nm)
1 | 190.1 | 1577.03
2 | 190.2 | 1576.20
3 | 190.3 | 1575.37
…. | … | 
72 | 197.2 | 1520.25
Wavelength multiplexing

## Slide 20
ITU grid for DWDM:
Old:
Spacing = 200 GHz ≈ 1.6 nm
Use only even or odd channel numbers
Current:
Spacing = 100 GHz ≈ 0.8 nm
Future:
Spacing = 50 GHz ≈ 0.4 nm
Use fractional channel numbers
Channel number | Central Frequency (THz) | Central wavelength (nm)
1 | 190.1 | 1577.03
1.5 | 190.15 | 1576.61
2 | 190.2 | 1576.20
Wavelength multiplexing

## Slide 21
Wavelength multiplexing
Cross talk =
Input power – isolation – directivity

## Slide 22
Wavelength multiplexing
Add drop WDM (aka single channel)
WDM
Common
Pass
Reject

## Slide 23
Wavelength multiplexing
Add drop WDM (aka single channel)

## Slide 24
Fibre Bragg Gratting
λBragg = 2nΛ

## Slide 25
Fibre Bragg Grating
λBragg = 2nΛ

## Slide 26
Fibre Bragg Grating

## Slide 27
WDM technologies
Cascading FBGs is not the best.
Thin Film | Arrayed Wave Guide
Good for few channels | Lower loss for many channels
Similar to Fabry–Pérot | Interferometric
Built by Vapour deposition or sputtering | Etched, optically or via CMOS

## Slide 28
AWG

## Slide 29
Optical Switch
Optical path switching (or optical matrix switching), Optical transistors and opto-mechanical switches are often confused.
Interferometer based photonic path switch
Mems or Piezo based

## Slide 30
Mems
Driven by magnetic fields or electrostatic fields
Difficult to damp out oscillations at high speed
Sub um prescision
Mems =micro-electromechanical system

## Slide 31
Piezo electric effect
Apply voltage to change crystal length.
Needs high voltage for even a few um
Sub nm precision

## Slide 32
Optical path switches
https://spectrum.ieee.org/optical-switch-1000x-faster-transistors
Optical transistors are fascinating! More about how they can build a 1000 times faster computer here
Interferometric | MEMS/Piezo
Good for few channels | Lower loss for many channels
Fast (>MHz) | Slow (<kHz)
Tiny but polarisation dependent | Large but polarisation independent
Can act as a BS (i.e. 1 to many) | 1 to 1 switching only

## Slide 33
ROADM
Reconfigurable Optical Add-Drop Multiplexer:
  add, block, pass or redirect signals

## Slide 34
ROADM
This is how we start to build real networks. More info EENGM0003 Optical Networks by George Kanellos

## Slide 35
Chapter 12: Optical Communications Essentials Gerd Keiser, ISBN 0-07-141204-2
Section 15.2.3 and section 15.4: Optical fibre communications Principles and Practice Third edition John M. Senior ISBN: 978-0-13-032681-2
Further reading

## Slide 36
Given the following constraints, what is the longest distance over which an NRZ OOK protocol can have at least 1Gbps of data rate.
Problems
Up to 20 EDFAs each with:
Min input power = -20dBm
Max input power = 0dBm
Tuneable gain <=40 dBm
Noise figure = 3.8dBm
1 units of OOK transmitters
with 10 dBm transmit power, 1 Gbaud/s and a transmit noise of -20dBm
1unit of OOK receivers:
0.4A/W responsivity 0.5nA of dark current and 5E-12 W/Sqrt(Hz) NEP, max bandwidth is 10GHz
Optical fibre:
SM, 0.2dB/Km,
No loss when connecting any other components.
Assume that the EDFAs are equally spaced and there is no additional EDFA before the receiver. Further assume that the maximum desirable launch power is 10dBm.
Will adding more EDFAs help improve the distance?

## Slide 37
Max launch power is 10 dBm and min receive power for next EDFA is -20dBm, So a max loss of 30dB is permitted.
At 0.2dB/km, we can have upto 150 km between EDFAs
With -20dBm of transmit noise, the best SNR of the transmitter becomes 10mW/10uW => SNR = 1,000 or 30dB.
When each EDFA has 3.8 dB Noise Factor. We can have int(30/3.8) = 7 EDFAs in the total length
150km*7 = 1050km
Problems
The 40dB gain of the EDFA is more than enough to boost the launch power back to 10dBm from -20dBm

## Slide 38
But the detector is sensitive up to:
Total noise in detector: 0.5nA + Sqrt(Bw)* 5E-12*0.4. The bandwidth is 1 GHz (since that is the transmit bandwidth) =63.7nA.
To be detected the signal must be > noise. So we need a signal strength of 63.7nA/0.4A/W = 1.59E-7 nW = -37.9dBm or more.
That means an additional -37.9/0.2 = 189.5km of fibre would be ok.
Total length = 1050+189.5 = 1,239.5 km
Problems
Normally we would want a better SNR but if it is not specified we can go with the bare minimum of 1

## Slide 39
Will adding more EDFAs help?
No. There is already too much noise from the EDFAs
If I could place Raman amplifiers with a gain of 15dB and effective NF of -1 along with each EDFA, how much longer could the total span be?
Problems

## Slide 40
With a Raman amplifier in place, the power before the EDFA is increased by 15dB
So that’s an additional 15/0.2 = 75 km between each EDFA.
Additionally the Raman amplifier would reduce the NF of each EDFA by 1dB
Problems
When each Raman-EDFA pair has (3.8-1) dB Noise Factor. We can have int(30/2.8) = 10 Raman-EDFA pairs in the total length
So the total fibre distance can be 10*(150+75)+189.5 = 2439.5 km
Wow, almost double!