## Slide 1: Optical communications and data networks (EENGM2001)
Siddarth K Joshi

## Slide 2
Approx 25 hour unit given by Siddarth K Joshi (sk.joshi@bristol.ac.uk)
10 Credit point module = 100+ hours of study:
12 hours of synchronous lectures (in person):
13 hours of Asynchronous (virtual lectures):
Minimum of 75 hours of self study.
Tuesdays: 15:00 to 15:30 Lectures.
15:30 to 16:00 Problems.

## Slide 3
Mondays: 10:00 am to 11:00 am : Introduce basic concepts
Tuesdays: 15:00 to 15:30 : Applications of these concepts
Wednesday to Friday: Asynchronous lectures
Lectures in Balckboard. Filename formats Week#_Sequence#_Sync/async_Topic
Must complete Async lectures for each week before next class on the following Monday.

## Slide 4
Evaluation:
Just one exam at end of semester (date and details to be announced)
Intended learning outcomes
Describe the key issues and building blocks in modern optical communications systems;
Describe optical transmitters and receivers, or transceivers, methods of modulating light wave carriers with digital data, and methods of demodulation.
Describe the main factors limiting the data transmission speed and distance in optical fibre communication systems;
Describe methods of overcoming above limitations to achieve higher data speed, longer transmission distances, and larger overall transmission capacities.
Describe and specify an optical communications system.
Outline future directions of technological developments in optical fibre communications.

## Slide 5
 | Reference | Comments
[1] | Agrawal, G. P. (2010) Fiber-optic communication systems. 4th edn. Hoboken, N.J.: Wiley. | The canonical resource
[2] | Cvijetic, M. (2004) Optical transmission systems engineering. Boston: Artech House (Artech House optoelectronics library). | Systems engineering
[3] | Rajiv Ramaswami & Kumar N. Sivarajan, ‘Optical Networks: A Practical Perspective’ 2nd Ed., Morgan Kaufmann, ISBN 1-55860-655-6. | Problems
[4] | Sibley, M. J. N. (2020) Optical communications : components and systems. 3rd edn. Cham: Springer. | Problems
[5] | I. Kaminow and T. Li, ‘Optical Fibre Communications, Ed. IV, B (systems and impairments) | Advanced Reading

## Slide 6
Lesson plan:
See Blackboard.
Components
Systems

## Slide 7
Open Systems Interconnection model (OSI model):
7 Layers
ISO/IEC 7498 a.k.a ITU-T Recommendation X.200
Introduction
Our main focus

## Slide 8
Functions:
Bit synchronization: The physical layer provides the synchronization of the bits by providing a clock. This clock controls both sender and receiver
Bit rate control: The Physical layer also defines the transmission rate i.e. the number of bits sent per second.
Physical topologies: Physical layer specifies the way in which the different, devices/nodes are arranged in a network e.g. bus, star, or mesh topology.
Transmission mode: Physical layer also defines the way in which the data flows between the two connected devices.
Physical layer

## Slide 9
Parts:
Physical layer
Transmitter
Medium
Receiver
Laser/LED
Modulator
Optical Fibre
Free space
Photodiodes
Homo/heterodyne detectors
Topics of interest:
Encoding data
Modulation Schemes
Security of information
Transmitter properties
Losses
Propagation errors
Amplifiers
Resource optimisation
Noise
De-modulation
Power budget

## Slide 10
All data is binary: i.e. 0s and 1s
Which layer translates between binary and human readable form?
The basics
Bit: Each 0 or 1 is a bit abbreviation b
Byte: 8 bits = 1 byte abbreviation B
Kilobyte: 1024 bytes abbreviation KB
Kilobit: 103 bits abbreviation Kb
Megabyte: 1024 KB abbreviation MB
Megabit: 106 bits abbreviation Mb
Kilo
Mega
Giga
Tera
Peta
Exa
Zetta

## Slide 11
Prevent others from reading your data
Ensure that you communicate with the right person/device
Make sure your message actually reaches
Security
Encryption
Authentication
Reliability

## Slide 12
Basic encryption
Alice encrypts
Bob decrypts.
Eve should not know anything.

## Slide 13
Basic encryption
Random key
Encryption needs a key (password)
The XOR operation
Message
11100010
01111011
10011001
Message
Key
Encrypted
Key
10011001
Eve gets randomness

## Slide 14
The problem is now distributing the key
  Use mathematical problems like Prime factorisation
Which layers does encryption happen?
  Hint TLS and SSL are the most commonly used protocols.
Security

## Slide 15
The problem is now distributing the key
  Use mathematical problems like Prime factorisation
Which layers does encryption happen?
  Hint TLS and SSL are the most commonly used protocols.
  Applications typically treat TLS as if it were running in the transport layer
  But requires handshake so it also needs the presentation layer
SSL Deprecated in 2015
TLS currently ver 1.3
Algorithm based security protocols have limited lifetime
Security
Handshake: a signal between devices for coordination. Typically used to enquire and confirm connection/signal status

## Slide 16
Data on networks is almost always compressed.
Compression: Identify patterns in data and save the patterns rather than the raw data to reduce number of bits.
We focus on the physical layer and thus do not care about the meaning of the binary data.
Compression

## Slide 17
Recap: What is a laser?
Balance between Spontaneous emission, absorption & induced emission Phase coherent output.
Wavelength linewidth depends on cavity, gain medium & output power
More in Week13 Lecture003_Async

## Slide 18
Wavelength Vs Frequency
Frequency f [Units Hz] {E.g. THz, GHz, MHz, KHz, mHz, etc}
Wavelength (lambda) λ [Units m] {E.g. nm, micron or μm or um}a
Speed of light in vacuum c
c = 299 792 458 m/s
We will always use the approximate value of c = 3E8 (3*108)
Conversion between f and λ is an ILO
What is the frequency of 1550.12 nm in THz?

## Slide 19
Light as a wave
  Polarization
  Amplitude A
  frequency n
  wave vector k
  phase f
  Power of light I ∝A2

## Slide 20
Polarisation
Direction of oscillation of Electric field.
When passing through a polarizer:
Malus’s Law
Another ILO

## Slide 21
Polarisation
Direction of oscillation of Electric field.
When passing through a polarizer: Malus’s Law
Can oscillate in any plane
Vertical
Horizontal
∣H 〉
∣V 〉
∣D〉
Diagonal
∣A〉
Anti-diagonal
∣L〉
∣R〉
Left and Right handed
Circularly polarized

## Slide 22
Wave number/vector
Wave vector (wave number) in vacuum
Wave vector (wave number) in a medium with refractive index n
Wavenumber k is not an independent parameter
k is the number of 2p phase shifts per unit propagation distance
Wave vector in a homogeneous medium with refractive index n
Wave vector in a waveguide (or other media with boundary conditions)
Dispersion relation
More about dispersion in Week 16

## Slide 23
Modulation
ILOs
Understand various modulation formats used in optical communications
Learn various methods and devices for realising optical modulation

## Slide 24
Modulation
Types:
Amplitude
Phase
Sub-Types:
On Off Keying (OOK), Amplitude Shift Keying (ASK)
Phase Shift Keying (PSK)
Both can be upgraded to Quadrature (Q) : QPSK, QAM

## Slide 25
Modulation
:

## Slide 26
OOK
  Very simple
  Amplitude modulation
  Cheap transmitter and receiver
  Requires clock synchronisation
  SNR degrades with loss

## Slide 27
OOK
Direct modulation of laser
Or
External amplitude modulator
OOK is also called Binary Amplitude Modulation

## Slide 28
Recap: Laser threshold
FPL1009s datasheet

## Slide 29
Direct modulation for OOK
Laser diode operated by a current source
Off state: Just below threshold
On state: Operating current
Using an off state of 0 mA is slower and more energy consuming
Max modulation bandwidth given by Capacitance (C), Inductance (L) and Resistance (R). Which form a filter.
Simplest low pass filter.
Cut off frequency (-3dB) is

## Slide 30
OOK formats
NRZ: Non Return to Zero. Pulse representing 1 stays in the high state for the entire clock cycle.
RZ: Return to Zero. The 1 pulse returns to the zero state within the clock cycle.
NRZ has narrower spectral bandwidth
RZ can have better performance at high data speed, and easier for clock recovery
Why is this?
T
τ1

## Slide 31
OOK formats
Because of the usually non-zero values of P0, the light is not completely ‘Extinct’.
Average transmitted power
is the duty cycle
D=1: NRZ code
D~0.3 – 0.5 for RZ code
Small p: probability of 0 or 1
Duty Cycle
Typically we have equal number of 0s and 1s

## Slide 32
OOK formats
‘Extinction Ratio’ is defined as
Optical modulation
amplitude is defined as
(NRZ)
general
OMA is the actually useful signal amplitude
Do not confuse OMA with OAM Optical Amplitude Modulator is a device
Prove this statement and derive the equivalent for RZ

## Slide 33
OOK Direct modulation of a LD
Ith
current
Optical
power
P0
P1
Ib
Slope efficiency
h=dP/dI
Pt
Idata

## Slide 34
OOK Direct modulation of a LD
It’s frequency response typically exhibits a 2nd order filter response
  a resonance peak fr
  3dB BW of up to 20-30 GHz can be achieved with carefully engineered LDs
Height of peak should be controlled
  Max 3dB BW is obtained at ‘critical damping’
Frequency of electrical current
Response of output optical power
fr
f3dB
BW
LDs have limited modulation response bandwidth

## Slide 35
OOK Direct modulation of a LD
Waveform distortion caused by
  BW limitation: slow rising and falling edges
  Relaxation osc.: resulting in thick ‘eye-lid’ in eye-diagram
Ideal current waveform
BW limited output waveform
Under-damped output waveform
Pulse
waveform
Eye diagram
More about eye diagrams tomorrow

## Slide 36
OOK Direct modulation of a LD
Low cost😀
Low waveform quality😢
Low spectral quality😢
Can only be used for short-reach optical communications links

## Slide 37
Using external modulators
We will discuss how modulators are used in the Asynchronous Lecture Week13_Lecture_011_Async_Modulators
This will draw on knowledge form optoelectronic devices and other courses.

## Slide 38
ASK
Each amplitude level represents one symbol
  Better than OOK
  Simple receiver
  Increased error probability (lower SNR)
Baud rate = number of symbols (L) per second
Data rate = Baud rate * log2(L)
We will calculate this error rate when we study demodulation and receivers

## Slide 39
ASK
4 symbols is typically a good choice
Graph calculated with common values of detection noise & loss. Assuming no intersymbol interference.
You will learn how to calculate this soon

## Slide 40
ASK
What laser do we need?
High carrier frequencies (either modulated lasers or high repetition rate pulsed lasers)
Where is it used?
Ethernet protocols (E.g., EEE 802.3ba 100Gb/s & IEEE P802.3bs 400Gb/s standards)
<10 Km or <40 Km links
≈ up to 25 GBd (Giga baud)

## Slide 41
Frequency Chirp
Frequency chirp: Rapid change in (modulation) frequency
Two types:
Change in modulation: due to imperfect shape of electric pulse.
    Change in wavelength: due to refractive index dependence of a semiconductor on the current flowing through it. This changes the optical path length of the laser cavity.
Also called parasitic phase modulation

## Slide 42
Frequency Chirp
Chirp: optical frequency change accompanying amplitude change
In direct modulation, Chirp is caused by current change, as n is function of current I
Typical value dn / dI ~ 120GHz/mA
Chirp broadens the optical spectrum
Chirp is bad for transmission because of fibre dispersion (discussed later)
This chirp happens to all lasers: even DFB laser will have chirp under direct modulation
Input current waveform
Output power waveform
Output frequency chirp
freq
t

## Slide 43
Frequency Chirp
Fix frequency chirp by modulating laser drive current
Complex fix
Strong limit on baud rate if not fixed.
A. S. Karar, et al. Optik, 206, 164308 (2020).

## Slide 44
Signal spectra
Pure amplitude modulation will create symmetric side-bands
The modulated signal BW is decided by the pulse width t: BW∝ 1/t1
NRZ: t1=T, (T: data clock period)， RZ: t1<T
Optical frequency
Spectrum before modulation
Spectrum is a d-function
Optical frequency
Spectrum after
NRZ modulation
BW = 2x (1/T)
BW
Optical frequency
BW
Spectrum after
RZ modulation
BW = 2x (1/t1)

## Slide 45
Signal spectra
Additional phase modulation (PM) or chirp will
  Broaden the spectrum of AM signals
  Make the spectrum asymmetric
Spectrum before modulation
Spectrum is a d-function
Spectrum after
NRZ modulation
No chirp
BW
Spectrum after
NRZ modulation
With chirp
BW

## Slide 46
Phase
Phase is always a relative measurement.
0 degree
180 deg or π
90 deg or π/2

## Slide 47
Phase coherence
A laser is phase coherent.
i.e. all light emitted from the laser at the same time has the same phase.
A laser’s phase drifts with time.
Phase measured by interference

## Slide 48
Interference
Light of same frequency and same polarisation can interfere.
Interference is the sum of the wave equations.
Light of different frequencies can interfere to give a beat frequency
https://ophysics.com/waves10.html
Beat frequency is the envelope
= |f1 – f2|

## Slide 49
Interference
Phase changes can be detected by interference.
Interfere a reference signal and the phase modulated signal to detect phase changes.

## Slide 50
PSK
Amplitude is affected by noise and loss.
Phase of carrier wave less so.
Binary PSK L = 2 (0 0°, 1 180°)
  Less sensitive to noise
  Good for long distance and lossy links
  Complex signal reconstruction Needs a local oscillator at carrier frequency.
    Can you think of this before we discuss it in Week 15?

## Slide 51
Problem
Convert a frequency difference of 100 GHz at 1550nm to the corresponding wavelength difference. State your answer in nm.
Hint: Frequency difference is f1 – f2 and is not the same as 100 GHz directly expressed in nm.

## Slide 52
Problem
A BAM scheme uses a signal amplitude of 0dBm for 1 and -10dBm for 0. With a duty cycle of 1. Calculate the average transmitted power.
With a time period of 1ns what is the frequency bandwidth of the modulator required?
If the duty cycle was 0.2 what would be the new average power and the new frequency bandwidth required for the modulator?
Explain the difference between the frequency bandwidth of the modulator and the optical bandwidth of the transmitted signal.