## Slide 1: Optical communications and data networks (EENGM2001)
Siddarth K Joshi

## Slide 2
Constellation diagrams
Optical field E=E0exp(jΦ)
Note: in electrical engineering is often represented with j. But in most other fields is commonly represented by i
Im(E)
Re(E)
Phase
4 ASK constellation diagram
Optical ASK is always unipolar!
All symbols have the same phase

## Slide 3
Constellation diagrams
All symbols have equal transmit power!
8PSK constellation diagram

## Slide 4
Constellation diagrams
Intensity modulation constellation diagram
Optical field
E=E0exp(jΦ)
E0
Equally spaced in intensity = unequally spaced in amplitude

## Slide 5
More about constellation diagrams
Complex Phasor =
Cos Phase allows negatives in constellation diagrams
No negative power

## Slide 6
QAM
Split information into two data streams Ak and Bk
Sin and Cos are 900 out of phase
Mix and transmit
For analogue fc is carrier frequency for us πfc is T – the symbol duration.

## Slide 7
QAM
For optical communication the carrier is split into two phase components and each is amplitude modulated separately

## Slide 8
QAM

## Slide 9
QAM
4QPSK has same constellation diagram as 4QAM

## Slide 10
QAM
Ghayal, V.S. and Jeyachitra, R.K., 2020. Efficient Eye Diagram Analyzer for Optical Modulation Format recognition using Deep Learning Technique. In Advances in Electrical and Computer Technologies (pp. 655-666). Springer, Singapore.

## Slide 11
Recap:PSK
Amplitude is affected by noise and loss.
Phase of carrier wave less so.
Binary PSK L = 2 (0 0°, 1 180°)
  Less sensitive to noise
  Good for long distance and lossy links
  Complex signal reconstruction Needs a local oscillator at carrier frequency.
    Can you think of this before we discuss it in Week 15?

## Slide 12
BPSK Eye diagram
Eye diagram is same as NRZ OOK. This is also a “2-state system”. Decoding the phase or the amplitude makes very little difference.

## Slide 13
QPSK
Quadrature PSK uses 4 symbols with a 900 phase difference.
Also called 4-PSK
Very similar to 4-QAM
No change in amplitude.

## Slide 14
QPSK Vs QAM
BASIS FOR COMPARISON | QAM | QPSK
Stands for | Quadrature Amplitude Modulation | Quadrature Phase-Shift Keying
Spectral width | Narrow | Wide
Number of transmitted bits | Depends on its type | 2 bits
Performance | Average | Better
Bit error rate | High | Low

## Slide 15
QPSK Eye diagrams
Not the same as 4-QAM,
In 4-QAM we have phase and amplitude change.
In QPSK there is just phase change.
Notes: High frequency loss.

## Slide 16
Recommended Reading
Agalliu, Rajdi, and Michal Lucki. "Benefits and limits of modulation formats for optical communications." Advances in Electrical and Electronic Engineering 12.2 (2014): 160-167.
https://core.ac.uk/download/pdf/84392529.pdf

## Slide 17
Problem
Convert a frequency difference of 100 GHz at 1550nm to the corresponding wavelength difference. State your answer in nm.
Hint: Frequency difference is f1 – f2 and is not the same as 100 GHz directly expressed in nm.
Thus,
However we note that a frequency difference of 100GHz when compared to the frequency of 1550nm light (~193.4 THz) is very small so
We need to find

## Slide 18
Problem
Draw Constellation diagrams for 8ASK, OOK
8 ASK OOK

## Slide 19
Problem
Why do we not use 16-PSK or 32-PSK etc? But still use 64-QAM?

## Slide 20
Problem
Dual-polarization quadrature phase shift keying (DPQPSK) or dual-polarization QPSK uses two different polarisations each of which are modulated with a QPSK scheme. If the two polarisations are 00 and 450 and the receiver uses a polariser mounted at 22.50 what fraction of each signal will the receiver see?
Is it possible to use a quad-polarisation QPSK scheme with a single monochromatic channel. Explain your answer.

## Slide 21
Problem
If the transmitter needs a minimum OMA of 100μW and the maximum transmit power is 3dBm, what is the highest value of x in an x-ASK scheme that this transmitter can support?
Notes: 6451.61 cm–1

## Slide 22
Problem
If the transmitter needs a minimum OMA of 100μW and the maximum transmit power is 3dBm, what is the highest value of x in an x-ASK scheme that this transmitter can support?
100 μW = -10dBm, 3dBm ~ 2mW.
2mW/100uW = 20. So we can have 20 amplitude levels.
But does 20-ASK make sense? No. to transmit 4 bits per symbol we need 16-ASK to transmit 5 bits per symbol we need 32-ASK. With just 20 symbols there will be bit combinations we cant transmit. So the highest permissible value of x is 16.
Notes: 6451.61 cm–1

## Slide 23
Transmission
Optical loss in the medium.
Transmitter
Medium
Receiver
Laser/LED
Modulator
Optical Fibre
Free space
Photodiodes
Homo/heterodyne detectors
There are many things that can cause errors like:
Loss, dispersion, background noise, birefringence, etc.
Today we only consider loss.
Notes: 6451.61 cm–1

## Slide 24
Fibre losses
Notes: 6451.61 cm–1

## Slide 25
Fibre losses
Intrinsic Loss:
Absorption
Scattering
Attenuation (dB/km)
Wavelength (μm)
Intrinsic Loss measured in dB/km.
Fibre attenuation coefficient
P0:Power before
Pz: Power after z km

## Slide 26
Fibre losses
Absorption:
Intrinsic: due to the material itself
Extrinsic: due to impurities
Avoiding impurities is a major challenge.
Hydrogen reacts with the fibre to create OH- ions. Protective coating helps.
Impurity Ion | Loss due to 1ppm of impurity (dB/km) | Absorption Peak Wavelength (um)
Fe2+ | 0.68 | 1.1
Fe2+ | 0.15 | 0.4
Cu2+ | 1.1 | 0.85
Cr3+ | 1.6 | 0.625
V4+ | 2.7 | 0.725
OH– | 1.0 | 0.95
OH– | 2.0 | 1.24
OH– | 4.0 | 1.38

## Slide 27
Fibre losses
Scattering:
Rayleigh
Brillouin
Stimulated Raman

## Slide 28
Fibre losses
Scattering:
Rayleigh
    Responsible for 96% of all loss in modern fibre optics
    Is why the sky is blue and sunsets red/orange
    Occurs when particles are <
I: measured scattered intensity, R: distance to observer, scattering angle measured, d: diameter of particle.

## Slide 29
Fibre losses
Scattering:
Rayleigh
    Responsible for 96% of all loss in modern fibre optics
    Is why the sky is blue and sunsets red/orange
    Occurs when particles are <
I: measured scattered intensity, R: distance to observer, scattering angle measured, d: diameter of particle.
This is a linear process!
Strong dependence on wavelength and particle size

## Slide 30
Fibre losses
Brillouin Scattering:
Non linear process
Photon interacts with small inhomogeneities in medium
Thermal energies (Phonon), EM wave-dipole interaction (Polariton), or collective spin excitation (Magnon) can be absorbed (anti-Stokes) or created (Stokes)

## Slide 31
Fibre losses
Brillouin Scattering:
Stokes = Lower energy
Anti-Stokes = higher energy.
Sensitive to temperature and strain.
Used for sensors.

## Slide 32
Fibre losses
Brillouin Scattering:
Lower energy Stokes component dominant at low and room temperature
Usually scattered in the backwards direction.
So far we have only talked about spontaneous Brillouin scattering.
There is also stimulated Brillouin scattering.

## Slide 33
Fibre losses
Stimulated Brillouin Scattering:
10m fibre 1W input
10m fibre 1.8 W input

## Slide 34
Fibre losses
Stimulated Brillouin Scattering:
Limit on max transmit power!
If you send > 100mW (20dBm) through a long fibre, almost all light will be back scattered.
For a 1% back reflection and standard 100GHz channel.
Thus typical launch powers are < ~5mW.

## Slide 35
Problem
Given Stimulated Brillouin Scattering (SBS) occurring in a long single mode telecom fibre, what is the maximum length of fibre that can be used without an amplifier, if the receive power must be at least -30dBm.
Assume that the acceptable threshold is
The loss of the fibre is 0.2dB/km.

## Slide 36
Fibre losses
Scattering:
Stimulated Raman
Interaction with vibrational levels of molecules
Isotropic scattering
If transmitting at multiple wavelengths, adds noise to other channels.
Raman shift is typically ~10 THz.
Brillouin shift is about 10 to 500 GHz

## Slide 37
Fibre losses
High transmit power (i.e. >10 mW or 10 dBm) is almost always a bad idea for long distance (i.e. >> 10 km) communication.

## Slide 38
Fibre losses
Notes: 6451.61 cm–1

## Slide 39
Fibre losses
Bending
Any bend causes strain.
This increases scattering
Data sheets specify different losses at different bend radii

## Slide 40
Fibre losses
Insertion loss
Difference in refractive index between fibre and air causes some light to be reflected at a boundary.
Typically ~ -0.2dB
Can be reduced by AR coating (Expensive, delicate)

## Slide 41
Fibre losses
Return loss
Back reflected light due to connectors/ends
Typically ~ -0.1dB
Can be reduced by AR coating (Expensive, delicate)

## Slide 42
Fibre losses
Splicing
Heat, melt and fuse the glass fibres together.
Always some loss, typically
0.3dB.

## Slide 43
Measuring Fibre losses
Optical Time Domain Reflectrometry (OTDR)
Send pulse of light, measure back reflected pulse.
Use time of flight to measure position.

## Slide 44
Measuring Fibre losses

## Slide 45
Measuring Fibre losses
Reading an OTDR result is a basic skill and an ILO.
You need to be able to identify the total loss, distance to major events, etc.

## Slide 46
Fibre properties
Mode field diameter (MFD):
For good coupling input beam diameter = MFD
Represents extent of light field in fibre.
MFD > core.
Part of light travels through cladding

## Slide 47
Fibre properties

## Slide 48
Fibre properties

## Slide 49
Fibre properties