## Slide 1: Selected Topics on IoT Networking
RPL Fundamentals Routing Protocol for Low-Power, Lossy Networks
(Pronounced “Ripple”)

## Slide 2: At the PHY layer…
A .15.4 physical topology.
Imagine node A being a data collection node
A
C
B
E
F
D

## Slide 3: RPL
The IETF-proposed standard for routing in 6LoWPAN LLNs
Fundamentally a Distance Vector protocol
Design Goals:
  Optimised for data collection (from any node to ‘A’) (MP2P: Multi-Point to Point)
  Claims to be optimized for Point to Multi-Point (P2MP) – From ‘A’ to any other node. Not everyone necessarily agrees with this claim
  At a stretch: Any node to any other node (P2P)

## Slide 4: DODAGs and Instances
RPL models the network as a Destination-Oriented Directed Acyclic Graph (DODAG)
RPL Instance: A collection of non-overlapping DODAGs that use the same Objective Function – more later)

## Slide 5: An Example DODAG
Arrows indicate path to collection point
“A” is called the DODAG “Root”
The Root is in charge of creating the DODAG.
Each DODAG has an ID: One of the root’s routable IPv6 addresses (not link-local)
Fundamentally, the root starts the network using administratively-configured parameters
A
C
B
E
F
D
Root

## Slide 6: Node Ranks
Each node’s “Rank” indicates the “distance” of the node from the Root
It’s OK for two nodes to have the same rank
A
C
B
E
F
D
Rank: 128
192
312
512
1024
1024

## Slide 7: Rank Computation
A node’s rank is computed as: The rank of the next hop on the path to the root + the quality of the link to this hop
(Think of “link quality” as distance)
Therefore:
The lower a node’s rank, the closer this node is to the root
In RPL terminology, the link quality is called “Link Metric”
Lower link metric: Better link
Nodes aim to minimize their own rank

## Slide 8: Example Rank Computation
Node C has two possible “parents” towards the root:
A: Link Metric 184
B: Link Metric 56
C will choose B as the next hop, since this leads to node C having a lower rank.
B is now called “preferred parent”
A
C
B
E
F
D
Rank: 128
192
248
512
1024
1024
Link Metric = 56
184

## Slide 9: Objective Functions
Q: How do we calculate Link Metrics?
A: RPL uses the concept of “Objective Function” (OF).
An OF defines how a device calculates its own rank, based on:
  The rank of its candidate parents and
  Network-related parameters / link metrics
The OF also defines how link metrics are computed. This could be e.g. based on latency or packet loss observed in a link
Link Metrics expected to change over time

## Slide 10: Objective Functions
RPL is modular: Some OFs are standardized, but new ones can be defined
Some examples:
  OF0: “Objective Function Zero”. Uses hop-count as the link metric.
  MRHOF: “The Minimum Rank with Hysteresis Objective Function”
Single OF to be used within each DODAG
Same OF to be used by all DODAGs within the same RPL Instance