## Slide 1: Optical Networks [EENGM0003]
Dr. George T. Kanellos
[gt.kanellos@bristol.ac.uk]

## Slide 2: Sub-wavelength switched networks
Why Optical sub-wavelength switched networks
Optical Packet Switched network
Optical Burst Switched networks

## Slide 3: Optical Switching
Optical Switching granularity
  Optical Wavelength Switching
    Whole wavelength is allocated for a connection pair
  Optical sub-wavelength switching
    Wavelength is shared between connection pairs
      Optical Packet Switching (OPS)
      Optical Burst Switching (OBS)
      Optical Orthogonal Frequency Division Multiplexing (O-OFDM)

## Slide 4: Optical WDM Switching Advantages and Disadvantages
Advantage:
  Guaranteed bandwidth
      Predictable communication performance
  Simple abstraction
    Reliable communication channel between end hosts
    No worries about lost or out-of-order packets
  Simple forwarding
    Forwarding based on Wavelength
    No need to inspect traffic

## Slide 5: Optical WDM Switching Advantages and Disadvantages
Disadvantage
  Wasted bandwidth
    Bursty traffic leads to idle connection during silent period
    Unable to achieve gains from statistical multiplexing
  Blocked connections
    Connection refused when resources are not sufficient
    Wavelengths maybe reserved but not used always
  Connection set-up delay
    No communication until the connection/wavelength is set up
    Unable to avoid extra latency for small data transfers
  Network state
    Network nodes must store per-connection information

## Slide 6
Why Optical Sub-Wavelength Switching ?
Spectral efficiency
  Sub-wavelength switching supports high granularity
    spectral efficiency
    improved network economics (smaller OXCs)
Multi-service traffic bursty in nature
  IP-centric network
WDM switched networks provide granularity only at wavelength level
Convergence of electronic and optical technologies (IP/packet)
  control and management integration and simplification (Optical and electronic packet switched domain)

## Slide 7
Traffic Statistics I
bin
bytes per bin
5
10
0
(one bin = 0.01 Second)
one source
bin
2000
4000
0
bytes per bin
1000 sources
Synthetic trace generated with Poisson distribution representing traditional traffic
Traditional traffic models have short-range dependence
The superposition of many sources behaves like white noise
information/time slot

## Slide 8
10
5
0
bytes per bin
bin
(one bin = 0.01 Second)
one source
2000
4000
0
bytes per bin
bin
1000 sources
Synthetic trace generated with self-similar statistics (Pareto distribution)
representing Internet traffic
Self-similar traffic models have long-range dependence
The superposition of many sources is still bursty
Traffic Statistics II
packets/time slot

## Slide 9
Impact of Self-similarity
WDM switched channels must have sufficient bandwidth to cope with peak transmission.
Possibility of shaping traffic flows by buffering at network admission points-enables network operation at higher peak to average loads
Packet switched networks must have sufficient buffering to cope with long bursts, but associated delay must be acceptable.

## Slide 10
Packet Switching
Each node needs to perform:
Routing
Forwarding
Switching
Buffering
Multiplexing
Synchronization
Data flows are divided in packets
Each packet is routed separately
packets are received, buffered, queued, and transmitted (stored and forwarded) depending on the link capacity and the traffic load on the network
Dynamic bandwidth allocation (statistical multiplexing)

## Slide 11: Packet switching principles
Application message (e.g. a file) is split up into packets
Each of these packets is carried by the “network layer” (e.g. Internet Protocol – IP)
  Header indicates the destination address, and other information
These packets are transported over each link by a protocol such as Ethernet
  “sync” fields identify start and end of frame
  Header contains Ethernet address rather than say IP address
  Cyclic Redundancy Check (CRC) – redundant digits used to check for errors
message generated by application
data
H
data
H
data
H
data
H
sync
CRC
sync
datagrams from e.g. IP
frames generated by e.g. Ethernet

## Slide 12
Optical Packet Structure
user payload
guard bands
header
transparent payload
header
transparent payload
time slot
multiples of fixed time unit
variable bit rate
routing & control
Key Points: Payload transparency
Fixed or variable length
In OPS the payload remains in the optical domain end-to-end
The header is processed at each node to determine the local address
Near term approaches involve opto-electronic processing
the header is detected and processed to activate the switch fabric
Header information can be at lower bit rate than payload

## Slide 13
Optical Packet Switching Scenarios
Optical Packet Switch as:
Core router: optimisation of network resources, label swapping.
Edge router: aggregation, QoS, isolation of optical/IP domains
OPS builds on an existing dynamically reconfigurable network, which uses OXCs to provide optical channels (wavelengths) through the OTN
Network partitioning, some wavelengths support legacy clients others optical packets
Edge
OPS
Edge
OPS
Optical Transport Network
OXC
Label
Switch Routers
Core
OPS
SONET
/SDH
SONET
/SDH

## Slide 14: Network concept
Opto-electronic in the edges, all-optical techniques in the core of the network
  in the edges : aggregation, classification, packetisation, traffic shaping and QoS
  in the all-optical core nodes :space switching, contention resolution with dedicated physical resources per QoS, regeneration
Optical bandwidth partitioning between circuit switching and packet switching
  circuit switching : some wavelengths dedicated
  packet switching : the rest of the optical band

## Slide 15
Core Node Functions
Input processing: label processing, activates control, power equalisation, synchronisation
Switching: activates path between switch input port and required output port
Output processing: adds new label, may change wavelength to match network
Buffering: stores packet when contention exists
Control: control switch fabric, with info from label and table
Routing table: stores routing information
.
.
.
.
.
.
Output
Processing
1
N
.
.
.
.
.
.
1
N
Input
Processing
Switching
Buffering
Electronic Control
Routing Table
N inputs (wavelength channels)
N outputs (wavelength channels)

## Slide 16: Power Equalisation
Packets from different fibres /different network paths
Individual packet amplitudes vary considerably
require equalisation on a packet by packet basis, ideally in the optical domain
2R/3R all-optical regeneration is an option depending on how this is achieved or very fast optical amplification techniques

## Slide 17
Synchronous (slotted) operation:
  payload fixed duration
  synchronisation required at switch input
  guard bands required for optical processing/switching
  buffering requirements well defined
Asynchronous (unslotted) operation:
  payload can vary in duration
    matches variable IP packet format
    duration may vary in multiples of small fixed time slots
  special switch matrix required to enable packets to be switched at any time
  no synchronisation required
  buffering more complex
  In both cases labels are processed electronically, switch is transparent to payload
Asynchronous or Synchronous ?

## Slide 18: Need for Synchronisation
If switching is synchronous, alignment or synchronisation is necessary to avoid packet fragmentation
Packets access the switch ports through different routes and hence the packet edges will not be time aligned at the switch fabric input.
Example values of factors affecting the phase of optical packets
1. Dispersion in link: Over 1530 -1560nm, 100km @ 20ns/nm/km = 60ns variation
2. Temperature changes in link: 25C variation, 100km @ 40ps/C /km = 100ns
3. Temperature variations (slow) & dispersion effects in optical buffers (fast)  5 -10ns
4. Slow clock variations due to drift in master clock - typically <1s over 1000 sec

## Slide 19
Example Synchronizer
High signal-to-noise ratio (SNR) - limited passive losses and periodic
amplification by optical gates
High ON/OFF ratio (extinction) of gates results in low crosstalk
Very fast operation (<1ns)
Passive
Compensation
DCF
FDL
Electronic Control
FDL
Fibre Delay
Lines
(FDL)
Optical
gates
Input
Output
48
32
16
0
0
0
4
1
2
3
12
8

## Slide 20: Avoiding synchronisation
Asynchronous
  The packets may or may not have the same size
  Packets arrive and leave the switch without being aligned
  Packet-by-packet switch action
  packet contention is generally higher because the behaviour of the packets is more unpredictable and less regulated
  For the same traffic load the link throughput is lower than slotted networks
Variable length packets and asynchronous operation:
  Enables simpler grooming of traffic and higher packetization efficiency
  Is compatible with IP and other emerging transfer modes
  The switch architecture should ensure asynchronous switching paths set-up
  Optical buffering requirements are increasing
  Implementation of packet start and packet end recognition function is required

## Slide 21: Switching Fabric Space- switched or Wavelength- routed
Require a non- blocking optical switch functionality (NxN)
Space- switched
  Space switch fabrics can be constructed using multi- stage architectures based on SOA or electro- optic (eg Lithium Niobate) technology
  SOA the main approach to achieve reasonable scalability
Wavelength- routed
  A tunable wavelength converter preceding a passive wavelength routing device (such as an AWG) perform the same function but provide better scalability
  Proof of principle demonstrated in laboratory

## Slide 22: Contention Resolution
In packet networks contention occurs when two or more packets at the switch input ports request connection to the same output port simultaneously
A number of techniques can be deployed on their own or in combination:
  Buffering: For example if two packets are in contention, one might be delayed for a packet period in a buffer (such as fibre delay line)
  Deflection routing: An extension of above where the network is used as a buffer, packets are deflected into the network (for example rerouting)
  Wavelength multiplexing: Contending packets are assigned different wavelengths so they can co-exist on the same output port

## Slide 23: How to avoid buffering in OPS : Deflection Routing
1
2
Inbound optical packet on Port #1, red wavelength
Final destination is X, routing table indicates that X is reached out of Port #2
But all wavelengths on Port #2 have packets queued
Packet is switched out of Port #3
3

## Slide 24: Optical Packet Switching Main Issues:
Main issues:
  Building an optical buffer
    Use networking scheme that can reduce requirements for buffering
      Very inefficient
  Reading bits (OE) conversion at very high speed
    Technology advancement
    Use synchronous transmission
    In bound clock transmission and recovery

## Slide 25: Optical Burst Switching
Optical burst switching:
  A compromise between optical circuit and optical packet switching
  The header precedes (on a special control channel) the burst of information
    Header (Control messages are) sent separately from data traffic
    True "out of band" signalling
    Control channels can operate at constant lower bit rate (eg. 620Mbps)
Data channels are completely “service transparent”
  The burst may comprise packets from different sources or clients (i.e. not a flow)
Switch resources are allocated just before the burst arrives
  Ideally this means a reduced demand on buffering

## Slide 26
OBS Controller
O/E/O
Switch
Fabric
1
1
2
2
2
1
Control
wavelengths
Data
wavelengths
Data bursts
Control packet
Control packet processing
(setup/bandwidth reservation)
Time offset
The burst is assembled at the edge and may comprise packets from different sources.
A control packet (header) precedes (by the “offset time”) the burst of information
Switch resources are allocated just before the burst arrives.
Variation of the offset time, gives design flexibility
Ideally the approach means a reduced demand on buffering and slower switches (ms)
Optical Burst Switching
Notes: Optical burst switching (OBS) is a packet switched technique in which bursts of data are switched through the network. Successive bursts can be multiplexed onto a single wavelength thus providing the efficiency and flexibility associated with statistical multiplexing.
OBS is distinguished from Packet Switching in that control (header) information is transmitted on separate channels (wavelengths) from the data. It was initially conceived as a technique that did not require buffering (contention resolution) at each node, thus giving greater realisabilty in the optical domain. However, in practice, the demands for QoS may require burst buffering.
The diagram shows the functionality of the node. At the edge of the network a burst is assembled for transmission; this may (for example) comprise a sequence of IP packets destined for a particular location. A control packet is then first transmitted (on a separate channel) to the network, with the information following at a later time (the offset). At the node the control packet is processed and resources are allocated within the switch to enable direct switcing of the following information burst. By varying the offset time, buffering requirements may be minimised.
For burst switching the switch fabric speed can be less than that required for direct packet switching.

## Slide 27: Optical Burst Switching : Basic Principle
OBS
OBS
OBS
NMS
OBS
OBS
OBS
1: Burst is electronically buffered at the edge
2: Path setup message is sent on control channel
Network Management system

## Slide 28: Optical Burst Switching : Basic Principle
OBS
OBS
OBS
OBS
OBS
OBS
1: Burst is electronically buffered at the edge
2: Path setup message is sent on control channel
NMS can be informed of path setup
NMS

## Slide 29: Optical Burst Switching : Basic Principle
OBS
OBS
OBS
OBS
OBS
OBS
1: Burst is electronically buffered at the edge
2: Path setup message is sent on control channel
3: Burst now travels down optical channel
NMS

## Slide 30
There are three variations of burst switching*
  In all 3 bandwidth is reserved at the burst level using a one-way process, and a burst can cut-through switches, instead of being stored and forwarded
Tell-and-go TAG: A source sends a control packet on a separate channel to reserve bandwidth (set switches) along the path. After the data burst is transmitted another control packet is sent to release the bandwidth.
in-band terminator IBT: each burst has a header (as in packet switching) as well as a terminator to indicate the end of the burst. Differs from packet switching, in that it is not store and forward, head of burst can be transmitted before tail is received.
reserve-a-fixed-duration RFD: a control packet is first sent to reserve bandwidth, followed by data after an offset time. The bandwidth is reserved for a duration specified by the control packet, which contains the burst length. Data is buffered at the source and does not wait at intermediate nodes for the control packet to be processed-thus no buffering needed.
OBS Techniques*
*Ref: C. Qiao, M. Yoo, "Choices Features and Issues in Optical Burst Switching", Optical Networks Magazine, April 2000.

## Slide 31: Optical Burst Switching Considerations
How we know when to tear down the connections?
Reserve-a-fixed-duration (RFD)
  Control message reserves path for duration of burst
Tell-and-go (TAG)
  Burst is sent immediately after connection request
  Release message clears down route
  Or…refresh packets used to keep route open
In-band-terminator (IBT)
  Similar to TAG, but only release message is in-band after data burst
OBS would appear to be an alternative to optical packet …
  Ability to eliminate optical buffers
  Or, if optical buffering is present, the ability to enhance QoS or lower packet drop probability using them
  Either way, OBS can use any optical buffer technique
    Optical delay lines, wavelength translation, deflection routing

## Slide 32: End of Session 7
Any questions?