## Slide 1
Examples for lectures
Mobile Communications 2019
Notes: 1

## Slide 2: Cellular Design
Adjacent cells cannot use the same set of frequencies.
The colour and shading patterns are used to represent unique frequency groups.
We observe a central green cell surround by an initial set of six cochannel cells (the centre of these cells forms a larger hexagon).
These six cells form the first-tier of cochannel interferers.
The pattern shown is based on a cluster group of three cells.
The cluster group (or cluster size) is normally denoted by the letter N.
The available radio resources are shared equally across a group of N cells (with N=3 in this example).

## Slide 3: Cellular planning and capacity
An operator is allocated a certain bandwidth allocation, based on the type of radio system being used
This radio bandwidth is sub-divided into a number of frequency groups.
The number of frequency groups is defined by the cluster size
Here N=4 and each frequency group has 3.75 MHZ bandwidth

## Slide 4: Example 1
An analogue cellular system has a total bandwidth of 5 MHz and operates with a cluster size of 7 and a cell radius of 12 km. The network comprises of 100 basestations and each voice channel requires 25 kHz. Assuming that each user represents a traffic load of 0.02 Erlangs. Calculate the total subscriber capacity in each cell. Next determine the total capacity in terms of subscribers per MHz per kilometre squared. Finally, what is the total subscriber capacity of the network?
Bandwidth divided in 7 frequency groups 5/7=0.714 MHz per cell
Calls per cell = 5/(0.025*7) = 28.57
Subscribers per cell = 28.57/0.02 = 1428.57
Assuming a call bandwidth of 25 kHz, the 5 MHz system has 5/0.025 channels (200 calls)
These channels are used over a cluster area of 7 * 452 km2 = 3164 km2
Thus, total capacity = 200/(5*3164) = 0.0126 calls/MHz/km2
Subscriber capacity = (0.0126/0.02) = 0.632 subscribers/MHz/km2
Total subscriber capacity = 1428.57*100 = 142,857
Total coverage area = 100 * 452 = 452,000 km2
N=7
R=12km
Total Bandwidth=5MHz
Channel bandwidth=25kHz

## Slide 5: Example 2
A digital cellular system has a total bandwidth of 15 MHz and operates with a cluster size of 4 and a cell radius of 2 km. The network compromises 20 basestations and each 200 kHz carrier is made up of 8 TDMA voice channels. Assuming that each user represents a traffic load of 0.02 Erlangs. Calculate the total subscriber capacity in each cell. Next determine the total capacity in terms of subscribers per MHz per kilometre square. Finally, what is the total subscriber capacity of the network?
Bandwidth divided in 4 frequency groups 15/4=3.75 MHz per cell
Calls per cell = 15/((0.200/8)*4) = 150
Subscribers per cell = 150/0.02 = 7500
Assuming a 200 kHz call bandwidth, the 15 MHz system supports a total of 15/0.025=600 calls.
These channels are used over a cluster area of 4 * 12.6 km2 = 50.4 km2
Thus, total capacity = 600/(15*50.4) = 0.794 calls/MHz/ km2
Subscriber capacity = (0.794/0.02) = 39.68 subscribers/MHz/ km2
Total subscriber capacity = 7500*20 = 150,000
Total coverage area = 20 * 12.6 = 252 km2
N=4
R=2km
Total Bandwidth=15MHz
Channel bandwidth=25kHz

## Slide 6: Example 3
A digital microcellular system has a total bandwidth of 15 MHz and operates with a cluster size of 7 and a cell radius of 160m. The network compromises 20 basestations and each 200 kHz carrier is made up of 8 TDMA voice channels. Assume that each user represents a traffic load of 0.02 Erlangs. Calculate the total call and subscriber capacity in each cell and for the entire network.
Bandwidth divided in 7 frequency groups 15/7=2.14 MHz per cell
Calls per cell = (15/(7*0.2))*8 = 85.71
Subscribers per cell =85.71/0.02= 4,285.7
Assuming a 200 kHz call bandwidth, the 15 MHz system supports a total of 15/0.025= 600 calls.
These channels are used over a cluster area of 7 * 0.0804 km2= 0.563 km2
Thus, total capacity = 600/(15*0.563) = 71.04 calls/MHz/km2
Subscriber capacity = (71.04/0.02) = 3,552 subscribers/MHz/km2;
Total subscriber capacity = 4,285.7*20 = 85,714
or = 3,552*20*0.0804*15 = 85,714
Total coverage area = 20 * 0.0804 = 1.608 km2
N=7
R=160m
Total Bandwidth=15MHz
Channel bandwidth=25kHz