## Slide 1: The Application Layer
HTTP Caching

## Slide 2: Browser Caching
When a browser downloads a web object, it saves a copy of the object locally.
The collection of previously downloaded objects is called “a cache”.
When the browser needs to display the same object to the user in the future, it may load the object from cache instead of downloading it!

## Slide 3: Web caches (proxy server)
user sets browser: Web accesses via cache
browser sends all HTTP requests to cache
  Object NOT found in cache (cache “miss”): Proxy downloads object from origin
  Object found in cache (cache “hit”): proxy returns object
goal: satisfy client request without involving origin server
client
proxy
server
client
HTTP request
HTTP response
HTTP request
HTTP request
origin
server
origin
server
HTTP response
HTTP response

## Slide 4: More about Web caching
cache acts as both client and server
  server for original requesting client
  client to origin server
typically cache is installed by ISP (university, company, residential ISP)
why Web caching?
reduce response time for client request
reduce traffic on an institution’s access link

## Slide 5: Caching example:
origin
servers
public
Internet
institutional
network
1 Gbps LAN
1.54 Mbps
access link
assumptions:
avg object size: 100K bits
avg request rate from browsers to origin servers:15/sec
avg data rate to browsers: 1.50 Mbps
RTT from institutional router to any origin server: 2 sec
access link rate: 1.54 Mbps
consequences:
LAN utilization: ???
access link utilization = ???
total delay = ???

## Slide 6: Caching example:
origin
servers
public
Internet
institutional
network
1 Gbps LAN
1.54 Mbps
access link
assumptions:
avg object size: 100K bits
avg request rate from browsers to origin servers:15/sec
avg data rate to browsers: 1.50 Mbps
RTT from institutional router to any origin server: 2 sec
access link rate: 1.54 Mbps
consequences:
LAN utilization: 0.15%
access link utilization = 99%
total delay = Internet delay + access delay + LAN delay = 2 sec + a lot + usecs
problem!

## Slide 7: Caching example: fatter access link
assumptions:
avg object size: 100K bits
avg request rate from browsers to origin servers:15/sec
avg data rate to browsers: 1.50 Mbps
RTT from institutional router to any origin server: 2 sec
access link rate: 1.54 Mbps
consequences:
LAN utilization: ???
access link utilization = ???
total delay = ???
origin
servers
1.54 Mbps
access link
154 Mbps
154 Mbps
Cost: increased access link speed (not cheap!)
public
Internet
institutional
network
1 Gbps LAN

## Slide 8: Caching example: install local cache
institutional
network
1 Gbps LAN
origin
servers
1.54 Mbps
access link
local web
cache
assumptions:
avg object size: 100K bits
avg request rate from browsers to origin servers:15/sec
avg data rate to browsers: 1.50 Mbps
RTT from institutional router to any origin server: 2 sec
access link rate: 1.54 Mbps
How to compute link
utilization, delay?
Cost: web cache (cheap!)
public
Internet

## Slide 9: Caching example: install local cache
Calculating access link utilization, delay with cache:
suppose cache hit rate is 0.4
  40% requests satisfied at cache, 60% requests satisfied at origin
origin
servers
1.54 Mbps
access link
access link utilization:
  60% of requests use access link
data rate to browsers over access link = 0.6*1.50 Mbps = 0.9 Mbps
  utilization = 0.9/1.54 = ~58%
average delay
  0.6 * (delay from origin servers) + 0.4 * (delay when satisfied at cache) =
  0.6 * (2sec + delta) + 0.4 (LAN delay) =
  ~ 1.2 secs
  less than over the 154 Mbps link (and cheaper too!)
public
Internet
institutional
network
1 Gbps LAN
local web
cache

## Slide 10: Conditional GET
Goal: don’t send object if cache has up-to-date cached version
  no object transmission delay
  lower link utilization
cache: specify date of cached copy in HTTP request
  If-modified-since: <date>
server: response contains no object if cached copy is up-to-date:
  HTTP/1.0 304 Not Modified
HTTP request msg
If-modified-since: <date>
HTTP response
HTTP/1.0
304 Not Modified
object
not
modified
before
<date>
HTTP request msg
If-modified-since: <date>
HTTP response
HTTP/1.0 200 OK
<data>
object
modified
after
<date>
client
server