## Slide 1: Optical Networks [EENGM0003]
Dr. George T. Kanellos
[gt.kanellos@bristol.ac.uk]

## Slide 2: Part 2
Wavelength Division Multiplexing (WDM) Networks

## Slide 3: Topics
Wavelength routing principles
Passive wavelength routing
Fixed Optical Add/Drop multiplexers
Static Optical cross connects

## Slide 4: Wavelength Path
C
A
B
D
E
C
A
B
D
E
A
B
D
E
F
C
l1
l1
l2
l2
l2
l2
l1
Each optical path is assigned a single wavelength from end-to-end e.g. A-F, l2
Wavelength reuse is possible, e.g. A-C, l1 and B-E, l1;
Wavelength blocking possible, the network management system must ensure this does not occur
Management system must look across whole network (to assign wavelengths), this can pose problems for large networks.

## Slide 5: Virtual Wavelength Path
C
A
B
D
E
C
A
B
D
E
A
B
D
E
F
C
l1
l1
l2
l2
l3
l3
Wavelength translation at each node
Wavelength assigned link-by-link i.e. locally
Each optical path a concatenation of different wavelengths
Wavelength blocking eliminated
More complex nodes with possible transmission limitations

## Slide 6: Necessity for Wavelength Conversion - Blocking
Wavelength routed networks: The channels are routed through the network according to wavelength
If a channel is blocking the path for another channel, wavelength conversion resolves blocking
1
2
1
2

## Slide 7: What is a Wavelength Converter?
It converts the wavelength of an optical channel to another wavelength, preserving the information encoded on the original input channel
w
a
v
e
l
e
n
g
t
h
c
o
n
v
e
r
t
e
r
i
n
p
u
t
s
i
g
n
a
l
@

1
o
u
t
p
u
t
s
i
g
n
a
l
@

2

## Slide 8: Optical wavelength converters (OWC)
Multiple technologies are possible
Example : OWC based on SOA
  s : modulated input signal
  p : continuous wave (CW)
  s and p interact due to FWM non-linear effect to generate new carriers :
FWM is transparent to the amplitude and to the phase of s
Limitations : s must be modulated at most 100 Gbit/s
Filter

## Slide 9: SOA-MZI wavelength converter
Cross Phase Modulation (XPM)
XPM induces phase change to new wavelength
MZI interferometer translates phase change in amplitude modulation

## Slide 10
space
switch
WP vs VWP nodes
demultiplexer
space switch
multiplexer
wavelength path
l conversion
space
switch
virtual wavelength path
demultiplexer
space switch
wavelength translator
coupler

## Slide 11: A WDM Ring Network
Main Features of Ring:
N(N-1)/2 wavelengths required to fully interconnect N nodes
Potential for high resilience

## Slide 12: Example
WP
  AB: λ1
  AD: λ2
  AC: λ1
  AE:λ1
  BD: λ1
  BE:λ3
  CD: λ1
  CB: λ3
  CE:λ2
  ED: λ1
A
B
C
D
E
λ1
λ2
λ2
λ1
λ1
λ1
λ3
λ3
λ1
λ1
λ3
λ3
λ2
λ2
Can you design the network as a virtual wavelength path implementation?

## Slide 13: Grating Based Optical Add-Drop Multiplexer
l1
lN
OADM
OXC
OADM
l1
lN
MUX
MUX
Terminal
Terminal
l con
OADM
  Single input fibre supporting multiple l
  Single output fibre supporting multiple l
    fixed
    reconfigurable
OADM
Add
Drop
Output ports
Input ports

## Slide 14: Wavelength Add/Drop Multiplexers
F
i
b
e
r
B
r
a
g
g
G
r
a
t
i
n
g
C
o
u
p
l
e
u
r
p
a
s
s
i
f
2
x
1
O
A
D
M
Drop function
Passive coupler 2x1
Add function
Sin
Sout
Add
Drop
FBG
Circulator
Circulator
FBG: Fibre Bragg Grating

## Slide 15: Static OADM I
Parallel architecture
All wavelengths are demultiplexed
Some wavelengths are terminated
Terminated wavelengths are preconfigured
Fixed losses
Bidirectional

## Slide 16: Optical Cross Connect (OXC)
l1
lN
OADM
OXC
OADM
l1
lN
MUX
MUX
l con
Two basic switching schemes can be adopted in an OXC:
  Space Switching
    Either at the input or output to perform routing in the space domain
  Wavelength Switching
    Takes advantage of the WDM techniques:
        Wavelength selection using passive devices
        Wavelength conversion - solves blocking problem (when two input channels with the same wavelength aim at the same destination)

## Slide 17: Optical Cross Connect (OXC)
space switch
demultiplexer
multiplexer
WDM fibre
systems
Add-drop ports
Dimensions: 32 fibres x 100 l’s/fibre = 3200 optical channels
17

## Slide 18: Static Cross Connect

## Slide 19: Static Cross Connect

## Slide 20: What about passive WDM routing?
Arrayed Waveguide Grating Router

## Slide 21: What about passive WDM routing?
Arrayed Waveguide Grating Router
Cyclical freq. operation

## Slide 22: What about passive WDM routing?
Arrayed Waveguide Grating Router
AWGR cyclic frequency operation allows bidirectional collision-less, buffer-less routing for any-to-any direct interconnection

## Slide 23
Wavelength routing, where wavelength defines the path (route) through the network
Fixed routing does not give flexibility, need for switching
Needs for reconfigurable OADM/OXC
Issues
Next session:
Dynamic cross connects