## Slide 1: Optical communications and data networks (EENGM2001)
Siddarth K Joshi

## Slide 2
Overcoming loss
Relay
Amplifier
Receiver
Electronic
Signal
Transmitter
End
End
Long latency
Can decode packet header and
Redirect
Latency: The time taken for a “packet” of information to reach the receiver

## Slide 3
Optical amplifier
Dopped Fibre Amplifiers
Semiconductor amplifiers
Raman Amplifiers

## Slide 4
EDFA
Dopped Fibre Amplifier
Erbium-Doped Fibre Amplifier (EDFA)
This is actually a densely packed region of metastable states
Uses stimulated emission
Just like a laser

## Slide 5
EDFA
Isolators prevent noise

## Slide 6
EDFA
Core pumped
Cladding pumped
Short fibre length
Low distortion
Good for ultra short pulses
Low gain
Expensive
High gain, High output power
Cheap pump diodes (MM)
Stronger dispersion effects

## Slide 7
EDFA
Cladding pumped
Need to ensure overlap of pump (in the cladding) and signal (in the core) modes

## Slide 8
EYDFA
Ytterbium (Yb) is co-doped as a sensitizer
Er > 5000 ppm reduces efficiency
Yb has a wide absorption band
Cheaper since the pump laser is not wavelength stabilised

## Slide 9
EDFA
More detailed level structure
Each of the earlier levels is actually a set of many
980nm pump more common:
  Easy to extract from output
1480nm pump:
  Directly excites metastable state
  Higher efficiency

## Slide 10
EDFA
If EDFAs need to be chained,
Gain must be flattened.
Typical EDFA gain with Silica fibre
Typical EDFA gain with ZrF4 fibre

## Slide 11
EDFA
Important parameters
Gain
Output saturation power
Max input power
Noise figure

## Slide 12
EDFA
Noise Figure =
If the amplifier is below saturation, why is the SNR not constant?
For an answer in dB convert the ratio to dB

## Slide 13
EDFA
Amplified Spontaneous Emission:
  High gain e- mostly in excited state
  Probability for high spontaneous decay is large
  Each spontaneous photon can be further amplified by the EDFA
  Quantum limited noise factor = 3dB
  980nm pumped noise factor typically ~3.1dB
  1480nm …. ~4.2dB

## Slide 14
EDFA
Problem:
Given a noise factor of 3dB (a theoretically perfect EDFA) and an initial SNR of 30, what is the maximum number of EDFAs that can be chained together before the SNR falls below 1?

## Slide 15
EDFA
Problem:
Given a noise factor of 3dB (a theoretically perfect EDFA) and an initial SNR of 30, what is the maximum number of EDFAs that can be chained together such that the final SNR >=1?
Noise Figure =
Final SNR = 1, Initial SNR = 30
Combined Noise figure = 30/1 = 14.7dB
So after 5 EDFAs the SNR is only 0.9, So we can use a max of 4 EDFAs in a chain!

## Slide 16
EDFA
Problem:
Given a noise factor of 3.1dB, a saturation output of 20 dBm, a gain of 30dB, a minimum input power of -20 dBm, a fibre loss of 0.2dB/km and an initial SNR of 50. What is the maximum distance of a fibre optic communication link if the receiver has a sensitivity of -40dBm. Assume a BPSK protocol at 1550nm.
Hint: don’t forget the max transmit power through a fibre

## Slide 17
EDFA
More information:
E. Desurvire , Erbium Doped Fiber Amplifiers, John Wiley (1994)
C. R. Pollock, Fundamentals of optoelectronics, Irwin (1995)

## Slide 18
Overcoming the signal degradation
If EDFAs limit us to a few thousand km how do we build longer links?
Relays!
Convert the signal to electronic, De-code to binary, Re-transmit.

## Slide 19
SOA
Semiconductor Optical Amplifier
  Like a laser, same gain medium, lower cavity reflectivity
Typically:
  Slow, (10MHz, >10ns pulse width)
  Electrically pumped
  Small & Cheap
  Low gain bandwidth
  Low gain (< 16dB)
  High Noise Figures (>5dB)
Ideal for short distances, urban networks, etc.
https://strathprints.strath.ac.uk/3536/1/JON_SOAs_in_packet_switching.pdf

## Slide 20
Raman amplification
Use Stimulated Raman Scattering for amplification
  Change the wavelength in the process
  Use the fibre length as an amplifier (Distributed amplification)

## Slide 21
Raman Scattering: Recap
Scattering:
Stimulated Raman
Interaction with vibrational levels of molecules
Isotropic scattering
If transmitting at multiple wavelengths, adds noise to other channels.
Raman shift is typically ~10 THz.
Brillouin shift is about 10 to 500 GHz

## Slide 22
Raman Scattering: Correction
Stimulated Raman
  Needs strong fields
  A strong enough field will make the process directional
  Polarisation dependent
  Pump and material dependent
Spontaneous Raman
Occurs for low intensities
Is isotropic
Polarisation dependency increases with power until threshold

## Slide 23
Raman amplification
Energy of pump scattered into energy of signal
High pump powers (> 0.5W)
Signal wavelength does not change

## Slide 24
Raman amplification
Peak at 13.2 THz
To amplify light at 1550nm, pump is at 1452 nm (13.2 THz below)
Broad gain width (~6THz or 48nm)
Why is the pump always at a lower wavelength?

## Slide 25
Raman amplification
Use multiple pump wavelengths to increase gain bandwidth

## Slide 26
Raman amplification
Counter pump is preferred
Co-Pump can cause excess signal leading to SBS

## Slide 27
Raman amplification
Noise sources:
Amplified Spontaneous Emissions (ASE)
Double Rayleigh Scattering (DRS)
Pump Laser Noise
Using a Raman amplifier in presence of high reflection can damage equipment
Typically, commercial Raman amplifiers use a test laser before turning on

## Slide 28
Raman amplification
Noise can be lower than the ASE limit of EDFAs (3dB)
Effective NF = NF of Raman Amp – NF of EDFA = -1dB Typically
https://www.sciencedirect.com/science/article/pii/S1110016820303501

## Slide 29
Optical amplification
Raman Amplifier
EDFA
Low gain ( <~20dB)
Expensive
Low Noise
Used to extend total span distances
Rarely used alone (Typically with an EDFA)
EDFA gain up to ~40dB
Impose limit on total span distances

## Slide 30
Hybrid Raman & EDFA

## Slide 31
Hybrid Raman & EDFA

## Slide 32
Raman amplification
E.g. Raman amplifiers used to demonstrate 64 Tbps link!
http://www.gazettabyte.com/home/2014/2/5/xtera-demonstrates-40-terabit-using-raman-amplification.html

## Slide 33
Undersea fibre optics
Extensive use of Raman amps & EDFAs
Multiple redundancies for pump lasers in each module
Repeaters every 60 to 100 Km
Longer the link closer the spacing
Generators on each end maintain a +ve or –ve DC potential of 3 to 15 kV and ~ 20kW

## Slide 34
Homodyne detection
Method of phase decoding
Interferometer converts phase changes into intensity fluctuation
Modulated signal in one arm, unmodulated in another
Needs carrier signal
A similar process can convert OOK to BPSK

## Slide 35
Heterodyne detection
Homodyne = same frequencies
Heterodyne = different frequencies
Can use a different phase stable laser as reference
Input fields are:
Combined intensity becomes
+
2+ 2+ *𝐸𝐿𝑜 cos()t + *𝐸𝐿𝑜 cos()t
DC component filtered out
Way too fast, not detected

## Slide 36
Heterodyne detection
In the end all that is seen is the term
*𝐸𝐿𝑜 cos()t
This is just the beat frequency.
Can detect frequency or phase changes
V. high power Local Oscillator fields used to improve detection of weak signals
Double the SNR of direct detection!
Input fields are:

## Slide 37
Heterodyne detection
Can be Shot noise limited
If LO is replaced by reference (i.e. carrier wave) then heterodyne becomes homodyne
The BS is commonly 99:1 not 50:50
This improves the signal sensitivity, but needs much higher LO powers.

## Slide 38
DPSK
Calculate the delay for a 40Gbps DPSK link at 1550nm. The refractive index of the waveguide is 1.6
The delay is the necessary path length difference.