## Slide 1: Optical communications and data networks (EENGM2001)
Siddarth K Joshi

## Slide 2
Recap:ASK
Each amplitude level represents one symbol
  Better than OOK
  Simple receiver
  Increased error probability (lower SNR)
Baud rate = number of symbols (L) per second
Data rate = Baud rate * log2(L)
We will calculate this error rate when we study demodulation and receivers

## Slide 3
m-ASK
m-ASK has m symbols.
Pulse amplitude modulation is an analogue technique.
Do not confuse with digital ASK.
Analogue comms engineers will often call 2-ASK as PAM4 when referring to digital transmission that’s because they are so similar.

## Slide 4
m-ASK
Inter symbol distance
P0
Pmax
Inter symbol distance = (P0-Pmax)/m
Large inter symbol distance = better SNR

## Slide 5
Eye diagrams
Perfect OOK eye diagram
Oscilloscope display in which a digital signal from a receiver is repetitively sampled and applied to the vertical input, while the data rate is used to trigger the horizontal sweep

## Slide 6
OOK eye diagram
Persistence view of an oscilloscope.
Colour represents the number of pulses/points
Averaged over millions of pulses

## Slide 7
Eye diagrams
Used to detect flaws in the transmission.
What is the flaw here?
Notes: High frequency loss.

## Slide 8
Eye diagrams
Impedance mismatch or back reflection from un-terminated fibre (stub)
Example of inter symbol interference
1.25 Gbps OOK, with a stub causing delay of 0.4 T
(T is duration of symbol pulse)
Notes: High frequency loss.

## Slide 9
Eye diagrams
If inter symbol interference is too strong then the eye diagram is a mess and not useful.
Slowing the baud rate will improve the eye diagram and allow better diagnostics.
1.25 Gbps OOK, with a stub causing delay of 1.6 T
(T is duration of symbol pulse)
Notes: High frequency loss.

## Slide 10
Eye diagrams
1-1 transition
0-0 transition
1-0
transition
0-1
transition
0-0 transition
1-0
transition
0-1
transition
T
NRZ modulation
RZ modulation
Notes: High frequency loss.

## Slide 11
Constellation diagrams
Optical field E=E0exp(jΦ)
Note: in electrical engineering is often represented with j. But in most other fields is commonly represented by i
Im(E)
Re(E)
Phase
4 ASK constellation diagram
Optical ASK is always unipolar!
All symbols have the same phase

## Slide 12
Constellation diagrams
All symbols have equal transmit power!
8PSK constellation diagram

## Slide 13
Constellation diagrams
Intensity modulation constellation diagram
Optical field
E=E0exp(jΦ)
E0
Equally spaced in intensity = unequally spaced in amplitude

## Slide 14
QAM
Split information into two data streams Ak and Bk
Sin and Cos are 900 out of phase
Mix and transmit
For analogue fc is carrier frequency for us πfc is T – the symbol duration.

## Slide 15
QAM
For optical communication the carrier is split into two phase components and each is amplitude modulated separately

## Slide 16
QAM

## Slide 17
QAM
4QPSK has same constellation diagram as 4QAM

## Slide 18
QAM
Ghayal, V.S. and Jeyachitra, R.K., 2020. Efficient Eye Diagram Analyzer for Optical Modulation Format recognition using Deep Learning Technique. In Advances in Electrical and Computer Technologies (pp. 655-666). Springer, Singapore.

## Slide 19
Recap:PSK
Amplitude is affected by noise and loss.
Phase of carrier wave less so.
Binary PSK L = 2 (0 0°, 1 180°)
  Less sensitive to noise
  Good for long distance and lossy links
  Complex signal reconstruction Needs a local oscillator at carrier frequency.
    Can you think of this before we discuss it in Week 15?

## Slide 20
BPSK Eye diagram
Eye diagram is same as NRZ OOK. This is also a “2-state system”. Decoding the phase or the amplitude makes very little difference.

## Slide 21
QPSK
Quadrature PSK uses 4 symbols with a 900 phase difference.
Also called 4-PSK
Very similar to 4-QAM
No change in amplitude.

## Slide 22
QPSK Vs QAM
BASIS FOR COMPARISON | QAM | QPSK
Stands for | Quadrature Amplitude Modulation | Quadrature Phase-Shift Keying
Spectral width | Narrow | Wide
Number of transmitted bits | Depends on its type | 2 bits
Performance | Average | Better
Bit error rate | High | Low

## Slide 23
QPSK Eye diagrams
Not the same as 4-QAM,
In 4-QAM we have phase and amplitude change.
In QPSK there is just phase change.
Notes: High frequency loss.

## Slide 24
Recommended Reading
Agalliu, Rajdi, and Michal Lucki. "Benefits and limits of modulation formats for optical communications." Advances in Electrical and Electronic Engineering 12.2 (2014): 160-167.
https://core.ac.uk/download/pdf/84392529.pdf

## Slide 25
Problem
Convert a frequency difference of 100 GHz at 1550nm to the corresponding wavelength difference. State your answer in nm.
Hint: Frequency difference is f1 – f2 and is not the same as 100 GHz directly expressed in nm.

## Slide 26
Problem
A BAM scheme uses a signal amplitude of 0dBm for 1 and -10dBm for 0. With a duty cycle of 1. Calculate the average transmitted power.
With a time period of 1ns what is the frequency bandwidth of the modulator required?
If the duty cycle was 0.2 what would be the new average power and the new frequency bandwidth required for the modulator?
Explain the difference between the frequency bandwidth of the modulator and the optical bandwidth of the transmitted signal.

## Slide 27
Problem
Draw Constellation diagrams for 8ASK, OOK

## Slide 28
Problem
Why do we not use 16-PSK or 32-PSK etc? But still use 64-QAM?

## Slide 29
Problem
Dual-polarization quadrature phase shift keying (DPQPSK) or dual-polarization QPSK uses two different polarisations each of which are modulated with a QPSK scheme. If the two polarisations are 00 and 450 and the receiver uses a polariser mounted at 22.50 what fraction of each signal will the receiver see?
Is it possible to use a quad-polarisation QPSK scheme with a single monochromatic channel. Explain your answer.

## Slide 30
Problem
What is the wave number of 1550nm light in vacuum and in a optical fibre of refractive index 1.5? Express the answer in cm-1
Notes: 6451.61 cm–1

## Slide 31
Problem
A laser with a resistance of 1kohm and stray capacitance of 100pF is being directly modulated for an OOK scheme. Calculate the max baud rate at a 3dB cut off for the NRZ and RZ schemes. (Assume that the resistance and capacitance values provided form a simple first order low pass filter)
The duty cycle for the RZ scheme is 0.5.
What is the Baud rate for the same laser directly modulated with a 4ASK and 16ASK scheme.
Notes: 6451.61 cm–1

## Slide 32
Problem
If the transmitter needs a minimum OMA of 100μW and the maximum transmit power is 3dBm, what is the highest value of x in an x-ASK scheme that this transmitter can support?
Notes: 6451.61 cm–1