## Slide 1: Optical communications and data networks (EENGM2001) Week14_Lecture014_ASync_Interferometers
Siddarth K Joshi

## Slide 2
Beam Splitter
Optical device to change the direction of a fraction of the input power.
Not dependent on wavelength, polarisation, etc.
Only in the ideal case

## Slide 3
Mach–Zehnder interferometer
Simple
Use with EOM to modulate phase, amplitude
We already discussed this in Week13_Lecture007_Async_ ModulationDevices
Difficult to stabilise
Hard to change path length

## Slide 4
Mach–Zehnder interferometer
Can be built in fibre as well
Compare two fibres together
Extensive use in photonic technologies

## Slide 5
Mach–Zehnder interferometer
Used to build optical switches
Extensive use in photonic technologies
Japanese Journal of Applied Physics 59, SOOB04 (2020)https://doi.org/10.35848/1347-4065/ab8f09

## Slide 6
Mach–Zehnder interferometer
Photonic technologies:
Small size,
Low energy,
No mechanical parts
Reliable
Fast (<<us switching time)
Can also do all optical processing of information

## Slide 7
Sagnac Interferometer
Always phase stable, any vibration affects both paths.
Very easy to build

## Slide 8
Sagnac Interferometer
Always phase stable, any vibration affects both paths.
Very easy to build in fibre and bulk
Converts phase modulation to amplitude
Used in sensing and navigation as well.

## Slide 9
Cavity
Fabry–Pérot interferometer is a type of cavity
The mirrors can be two surfaces of a single material (Etalon) or two different mirrors.

## Slide 10
Cavity
Free spectral range =
Finesse =
Line width =

## Slide 11
Cavity
Optical power builds up in the cavity
Power in cavity = input power * Q-factor
Q-Factor =
Reflectivity
Q-Factor
1mm spacing, 1550nm

## Slide 12
Cavity
Good for spectral filtering
Can also be made from thin films
nm thick layers deposited one by one to form cavities.

## Slide 13
Michelson interferometer
Same principle as MZI
Folded path makes it easy to build.
Can measure laser coherence length (i.e. spectral linewidth)
Easy to change path length.
Main application: Optical interleaver

## Slide 14
Optical Interleaver
Combines pulses with different timing into a single output stream
(a type of multiplexing)
Compresses the wavelength bandwidth of both signals to increase the capacity of the channel

## Slide 15
Optical Interleaver
Uses a Gires–Tournois etalon as one mirror of the Michelson interferometer
Gires–Tournois etalon:
High reflectivity for both surfaces
Causes a strong phase dependence on wavelength
Uses a Gires–Tournois etalon as one mirror of the Michelson interferometer
The exact workings of the interleaver are too complex for this course

## Slide 16
Optical Interleaver
Uses a Gires–Tournois etalon as one mirror of the Michelson interferometer
Gires–Tournois etalon:
High reflectivity for both surfaces
Causes a strong phase dependence on wavelength