## Slide 1: Optical communications and data networks (EENGM2001) Week15_Lecture017_ASync_DispersionManagement
Siddarth K Joshi

## Slide 2
As the transmission link length is increased by optical amplification, dispersion accumulates.
For single channel transmission, fibres with opposite dispersion can be used in each span to achieve zero accumulated dispersion
For WDM transmission, dispersion of channels in the centre as well as at edges of the band needs to be compensated to acceptable levels
Dispersion slope is therefore important
Optical diesperson compensation: General Principles

## Slide 3
Dispersion compensating fibre (DCF)

## Slide 4
In systems it is the total accumulated dispersion DxL that decides the pulse broadening.
DCF can provide up to -1360 ps/nm compensation, sufficient for SMF span of 80km
However DCF has high loss (9 dB for -1360ps/nm)
When NZ-DSF with negative dispersion (about -3 ps/nm-km) is used, SMF can be used to compensate its dispersion. The span would consist of about 28% of SMF (17ps/nm-km) and 72% of negative dispersion NZ-DSF (-3 ps/nm-km).
This is used for submarine systems but not for terrestrial systems
Dispersion profile (ps/nm-km)
Accumulated Dispersion (ps/nm)
SMF
DCF
L
Dispersion Map & dispersion compensation for single channel using different types of fibre

## Slide 5
1550 nm
1600 nm
1500 nm
Dispersion D of Positive and negative NZ-DSFs
When negative NZ-DSF is used as transmission fibre, its dispersion may be compensated by using SMF
NZ-DSF

## Slide 6
If the total optical bandwidth of the WDM signal is L, transmission fibre has a dispersion of D at centre of band and dispersion slope of D’ (ps/nm2-km), then after span length L the dispersion difference between the lowest and highest wavelength is LD’L (ps/nm).
L
LD’L
l
Dispersion map for WDM channels compensated by a constant negative dispersion
Dispersion slope compensation

## Slide 7
where DT and DC are the dispersion of transmission and compensation fibres. The dispersion at edges of the wavelength band accumulated after the span compensation is
If a fibre with opposite dispersion is used to compensate the dispersion for the central channel, we have
In order for this to be zero, it is required that the relative dispersion slopes (RDS) of both fibres
match each other. Otherwise there will be a walk-off in accumulated dispersion.
Intro

## Slide 8
…But it is not always possible to have RDS matching. This is particularly problematic for submarine systems as they use negative dispersion fibres in the upper left quadrant, but no fibre is available in the lower right quadrant.

## Slide 10
Nonlinear effects (XPM, FWM) are severe when accumulated dispersion is small due to channels being synchronous with each other over longer distances.
It is therefore useful to have large local dispersion, but small total dispersion.
This can be done by allow dispersion to accumulate for half of the link length, over compensate it in the middle, then allow it to reach zero by end of link length.
Nonlinearity and 50/50 Compensation

## Slide 11
Chirped fibre grating can be engineered to give any desirable dispersion performance.
The dispersion-bandwidth product (which = the total delay) is fixed for a fixed length grating (~ 10 ns / m).
So in order to compensate large dispersion over wide bandwidth, long CFGs are needed.
input
output
Chirped fibre grating
frequency
delay
Reflected wavelength
=
2x grating period
Dispersion compensation using chirped fibre grating

## Slide 12
vg(m) is the group velocity of mode m.
Fourier transform of such impulse response will give a low pass filter characeristics. Therefore fibre group delay dispersion limits the bandwidth of the fibre.
When this model is applied to single mode fibre, vg is a continuous function of frequency or wavelength. The sum becomes an integration over the spectral range of the signal.
‘FIR response’
Electronic Dispersion Compensation (EDC)

## Slide 13
The effect of dispersion can be compensated by making a filter in the receiver.
Continuous time filters (CTF):
  Lift the high frequency response of the Transimpedance amplifier to give an overall broader bandwidth to the system.
  But this can be limited by SNR if the system has noise (e.g., EDFA)
f
detected optical signal spectrum
receiver response
output signal spectrum
Noise floor
Poor SNR
EDC

## Slide 14
Digital transversal filters
EDC

## Slide 15
The transversal filter can be seen as doing the opposite of the dispersion:
  it returns the dispersed impulse reponse back into a single output impulse.
This can be done by adjusting the delay and weight of each arm of the transversal filter
  Works for a fixed dispersion
  But needs to be adaptive
EDC

## Slide 16
Feed-forward equalizer (FFE) and /or decision feedback equalizer (DFE):
  FFE focuses more on removing distortion prior to a symbol’s main energy point (also called the pre-cursor area)
  DFE compensates for the interference following a symbol’s main energy point (also called the post-cursor area)
FFE
DFE
EDC

## Slide 17
Self-adaptive:
  An EDC chip has to be able to adapt to a range of dipsersion characteristics
  e.g: For SMF and MMF, dispersion characteristics very different
Standardisation:
  SMF long reach systems
  MMF/SMF10GbE systems
EDC implementation

## Slide 18
Dispersion causes pulse spreading
  Reduction in the pulse amplitude
  Reduction in SNR due to ISI
Dispersion causes a receiver sensitivity power pensalty
  Acceptable levels between 1 to 3 dB
  This PP needs to be included in system power budget
  Different acceptable levels of PP limit the transmission distance
Dispersion: effects and how to deal with it

## Slide 19
Signal spectral width:
  when it decided by the light source spectral width ( hence independent of data rate): BDLDl is constant.
  When using narrow spectral source+external modulation: B2DL is constant.
Data pulse format
  RZ or NRZ have different levels of tolerance to dispersion
  RZ more tolerant
Dispersion limited transmission distance

## Slide 20
Optical compensation
  Using fibres with opposite D
    SMF+DCF
    NZ-DSF (with –D) + SMF
  Dispersion map
  Diespersion slope compensation: relative dispersion slope (RDS) matching
  Using chirped fibre grating
Electronic Dispersion compensation (EDC)
Dispersion compensation