## Slide 1: Optical communications and data networks (EENGM2001) Week16_Lecture022_ASync_dB
Siddarth K Joshi

## Slide 2
dB Vs dBm Vs linear units
dB | dBm | Linear units
Is a relative unit. Represents the ratio between two quantities | Is an absolute unit referenced to 1mW of optical power | Is an absolute unit
Is similar to percentage | Tells you the order of magnitude of the optical power | Tells you the exact value
 | Is the number of dB when compared to mW Hence dBm | 
It is possible to reference the signal to a Watt instead so you get the unit dBW

## Slide 3
Problem
If I have 20dBm of optical power in channel 1 and 10 dBm of optical power in channel 2, both travelling along the same fibre. What is the total power in the fibre?

## Slide 4
Problem
No it is not 30dBm
20dBm is 100 mW 10dBm is 10mW the total power is 110mW = 20.414 dBm
Remember

## Slide 5
Problem
Also note that
When you add or subtract dB or dBm you are multiplying or dividing respectively.
30dBm is 1W (1000mW) of optical power this is most certainly not the result of combining 100mW and 10mW of power

## Slide 6
Problem
All the below are equivalent
Input power (I) | 20dBm | 100mW | 100mW
Output power (O) | 10dBm | 10mW | 10mW
Loss (L) | 10dB | 90% | 0.9
Transmission (T) | -10dB | 10% | 0.1
Calculation to get output from input and loss | O = I-L | O=I – L*I/100 | O=I – L*I
Calculation to get output from input and transmission | O= I+T | O = I*T/100 | O = I*T

## Slide 7
How to know when things went wrong
Dimensions are the most important thing. Always keep track of Units and Dimensions
When units and dimensions don’t match then you have done the problem wrong!
E.g. Input power = 30dBm output power = 1mW Transmission = ?
If you do Transmission = output/input = 1/30 Then you are wrong. Why?
Because there is no such unit as dBm/W
Dimension of dBm is nothing! dBm
Units already cancel out…

## Slide 8
How to know when things went wrong
E.g. 2:
Input power = 20dBm, Beam waist = 10 micorns, what is the intensity?
If you do 20[dBm]/(3.1415* 10[micron]*10[micron])
Then you get dBm/unitArea.
So instead of 100mW/(3.1415* 10[micron]*10[micron]) you get the wrong answer because you divided a Logarithm

## Slide 9
How to know when things went wrong
But you divided dBm and dB etc…
E.g. Each EDFA has a noise figure of 4 dB and the total SNR is 50dB, how many EDFAs can you use?
You did 50dB/4dB… That is dividing logs, surely that was wrong?
No I was adding/subtracting. Each EDFA causes 4 dB of noise. 2 EDFAS = 4+4 dB of noise, 3 EDFAs = 4+4+4, and so on
What you cannot do is divide dBm with dB or vice versa

## Slide 10
Exploit units
Units are always on your side! They give you important clues.
E.g. convert 200nm to Hz.
Don’t remember the formula? No problem, nm has dimensions of m Hz has dimensions of 1/s
Hmm… I what could possibly relate meters and seconds?
Hard to think of anything except speed or velocity right?
Now do you know the correct conversion?

## Slide 11
Exploit units
It works even in the most complex cases.
With an NEP of 8nW/ and responsivity of 0.1A/W how much electronic noise would you expect while using a modulation rate of 3Gbaud/s?
Forgot the formulae? Does not matter. Look at the units. You need to get something that is Sqrt(Hz). There is only one possible candidate.
W is not a unit of electricity so….
Again there is only one possible way to get the correct dimesions