## Slide 1: Optical communications and data networks (EENGM2001) Week16_Lecture023_ASync_SysEngProblemsAreEasy
Siddarth K Joshi

## Slide 2
Where to start?
I give you a bunch of data sheets and ask you to calculate something completely different, where do you start?

## Slide 3
Problem
E.g. I want to create a low latency 10Gbps link between A and B. These two places are 10,000km apart on the earth’s equator. Which components would you use to build this link and how? (Multiple copies of each instrument are available)
Fibre: (@1550nm)
0.15dB/km loss
15ps/nm/km dispersion,
Refractive index = 1.5
Max transmit power = 10dBm
EDFA:
NF = 3dB
30 dB gain,
-30 dB min input
20dBm saturation
Transmitter: BPSK
SNR = 100
Output power: 1dBm
Optical bandwidth 0.4nm
10Gbaud/s, latency 1ms
Transmitter: 16-ASK
SNR = 300
Output power: 10dBm
Optical bandwidth 0.8nm
2.5Gbaud/s, latency 2ms
Receiver: Both BPSK and m-ASK
Responsivity = 1A/W
Dark current = 20nA
Latency 2ms
0.2m dia telescope
Geo stationary satellite
0.1m dia telescope
Orbital height 35,800km
Can house same receiver, transmitter and or EDFAs

## Slide 4
Problem
E.g. I want to create a low latency 10Gbps link between A and B. These two places are 10,000km apart on the earth’s equator. Which components would you use to build this link and how? (Multiple copies of each instrument are available)
Fibre: (@1550nm)
0.15dB/km loss
15ps/nm/km dispersion,
Refractive index = 1.5
Max transmit power = 10dBm
EDFA:
NF = 3dB
30 dB gain,
-30 dB min input
20dBm saturation
Transmitter: BPSK
SNR = 100
Output power: 1dBm
Optical bandwidth 0.4nm
10Gbaud/s, latency 1ms
Transmitter: 16-ASK
SNR = 300
Output power: 10dBm
Optical bandwidth 0.8nm
2.5Gbaud/s, latency 2ms
Receiver: Both BPSK and m-ASK
Responsivity = 1A/W
Dark current = 20nA
Latency 2ms
0.2m dia telescope
Geo stationary satellite
0.1m dia telescope
Orbital height 35,800km
Can house same receiver, transmitter and or EDFAs

## Slide 5
Problem
Yikes! Where do I start?

## Slide 6
Problem
Look at what information is given and what information is not.
Think, what is the limiting factor?
What is being asked, what are the processes involved in each of the steps?

## Slide 7
Problem
E.g. I want to create a low latency 10Gbps link between A and B. These two places are 10,000km apart on the earth’s equator. Which components would you use to build this link and how? (Multiple copies of each instrument are available)
Fibre: (@1550nm)
0.15dB/km loss
15ps/nm/km dispersion,
Refractive index = 1.5
Max transmit power = 10dBm
EDFA:
NF = 3dB
30 dB gain,
-30 dB min input
20dBm saturation
Transmitter: BPSK
SNR = 100
Output power: 1dBm
Optical bandwidth 0.4nm
10Gbaud/s, latency 1ms
Transmitter: 16-ASK
SNR = 300
Output power: 10dBm
Optical bandwidth 0.8nm
2.5Gbaud/s, latency 2ms
Receiver: Both BPSK and m-ASK
Responsivity = 1A/W
Dark current = 20nA
Latency 2ms
0.2m dia telescope
Geo stationary satellite
0.1m dia telescope
Orbital height 35,800km
Can house same receiver, transmitter and or EDFAs

## Slide 8
Problem
Fine, so you want me to calculate latency,
Its obvious that some latency will be due to the speed of light
And then there are a few ms due to the transmitter and receiver, so what?
Good, that was step1 now what are the limitations?
That’s right you need an acceptable SNR

## Slide 9
Problem
Be careful of the units don’t confuse a SNR of 100 with an SNR of 100dB
So, I have been given different transmitters so they probably make a difference…
Clearly I am being asked to look at BPSK and 16 ASK over fibre vs via satellite.
Is there any sense combining a satellite with fibre? Will that help reduce latency?
No….

## Slide 10
Problem
Is there sense in combining BPSK with 16ASK?
Also would I even need to?
Well the EDFAs do impose a distance limit, then I need a relay
Distance limit, lets calculate… Is it the same for BPSK and 16 ASK?
Is the increased distance (if any) worth the extra 1ms of the 16-ASK transmitter?

## Slide 11
Problem
E.g. I want to create a 1550nm low latency 10Gbps link between A and B. These two places are 10,000km apart on the earth’s equator. Which components would you use to build this link and how? (Multiple copies of each instrument are available)
Fibre: (@1550nm)
0.15dB/km loss
15ps/nm/km dispersion,
Refractive index = 1.5
Max transmit power = 10dBm
EDFA:
NF = 3dB
30 dB gain,
-30 dB min input
20dBm saturation
Transmitter: BPSK
SNR = 100
Output power: 1dBm
Optical bandwidth 0.4nm
10Gbaud/s, latency 1ms
Transmitter: 16-ASK
SNR = 300
Output power: 10dBm
Optical bandwidth 0.8nm
2.5Gbaud/s, latency 2ms
Receiver: Both BPSK and m-ASK
Responsivity = 1A/W
Dark current = 20nA
Latency 2ms
0.2m dia telescope
Geo stationary satellite
0.1m dia telescope
Orbital height 35,800km
Can house same receiver, transmitter and or EDFAs

## Slide 12
Problem
The rest is easy a direct application of the formulae you have learnt.
The questions we have asked ourselves to solve this problem are the essence of systems engineering.