## Slide 1: Selected Topics on IoT Networking
IPv6

## Slide 2: IPv6 Addresses
128-bit address space: 2128 unique addresses
That’s approxmately 3.4×1038
2001:db8:85a3:0:0:8a2e:370:7334
“340 trillion trillion trillion”
“A few trillion addresses / person on Earth”
“252 addresses for every observable star in the known universe.”

## Slide 3: IPv6 Address Text Representation
128 bits = 16 bytes.
Eight groups of four hexadecimal digits, each group representing 2 bytes
The groups are separated by colons “:”
2001:0db8:85a3:0000:0000:8a2e:0370:7334
2 Bytes

## Slide 4: IPv6 Address Text Representation
2001:0db8:85a3:0000:0000:8a2e:0370:7334
Leading (insignificant) zeros within each group can be eliminated, but each group must show at least 1 digit.
2001:db8:85a3:0:0:8a2e:370:7334
It is very common to encounter long all-zeros sequences. We can replace 1 or more consecutive groups of all zeros with “::”. This can only be done once in each address. Why?
2001:db8:85a3::8a2e:370:7334

## Slide 5: IPv6 Address Classification
An IPv6 address can be:
Unicast: Identifies a single network interface
Anycast:
  Assigned to a group of interfaces, usually belonging to different nodes.
  A datagram sent to an anycast address is delivered to just one of the member interfaces, typically the “nearest” host.
  Anycast addresses cannot be identified easily, they have the same format as unicast addresses, and differ only by their presence in the network at multiple points.
Multicast:
  Also used by multiple hosts.
  Datagrams sent to a multicast address will be received by all interfaces that are members of the group.

## Slide 6: IPv6 Address Scopes
Each IPv6 address also has a scope. It specifies the part of the network where this address is valid.
Interface
Link: One hop away
Organisation
Global

## Slide 7: IPv6 Address Scopes
For example:
Link-local:
  These addresses can only be used on a single directly attached network (link).
  Essentially this makes them valid only within a single hop.
  IPv6 datagrams with a link-local destination address will never get routed beyond one hop.
  Useful to talk to immediate neighbors.
Global (or Universal):
  Valid in the entire network and globally routable.

## Slide 8: Generic Concept
Not very dissimilar from IPv4, just different terminology.
Fundamentally, there is a network part and a host part.
Length (bits) | 64 |  | 64
Link-local (unicast) | fe80:: |  | Interface Identifier
Link-local Example | fe80:: |  | 0:8a2e:370:7334
 | fe80::8a2e:370:7334 |  | 
Length (bits) | 48 | 16 | 64
Global (unicast) | Routing Prefix | Subnet ID | Interface Identifier
 | Network Prefix |  | 
Global Example | 2001:db8:85a3 | 0 | 0:8a2e:370:7334
 | 2001:db8:85a3::8a2e:370:7334 |  | 

## Slide 9: SLAAC
StateLess Address Auto-Configuration (SLAAC)
A device will use SLAAC to automatically assign unicast IPv6 addresses to its own interfaces
Interface ID is generated from the EUI-64 (or EUI-48 / MAC-48 after conversion to EUI-64)
The meaning of the U/L bit is inverted:
  0: Now means local
  1: Now means universal
SLAAC can be used to generate a link-local and a global address

## Slide 10: SLAAC Examples
Directly from EUI-64 | 
EUI 64 | 00:12:4B:00:18:75:69:A5
Link-local | fe80::212:4b00:1875:69a5
Global, for prefix 2001:db8:85a3::/64 | 2001:db8:85a3::212:4b00:1875:69a5
From 48-bit MAC address after it is converted to EUI-64 | 
MAC Address (EUI-48) | 00:0C:29:0C:47:D5
Convert to EUI-64: Insert FF:FE in the middle | 00:0C:29:FF:FE:0C:47:D5
Link-local | fe80::20C:29FF:FE0C:47D5
Global, for prefix 2001:db8:85a3::/64 | 2001:db8:85a3::20C:29FF:FE0C:47D5

## Slide 11: Multicast Scopes
Address | Scope | Notes
ff00::/16 ff0f::/16 | Reserved | 
ffx1::/16 | Interface-local | May not be sent over any network link. This is the multicast equivalent of the unicast loopback address.
ffx2::/16 | Link-local | May not be routed. All devices within a single hop
ffx3::/16 | Realm-local | Just for your reference
ffx4::/16 | Admin-local | The smallest scope that must be administratively configured.
ffx5::/16 | Site-local | Restricted to the local physical network.
ffx8::/16 | Organization-local | Restricted to networks used by the organization administering the local network.
ffxe::/16 | Global scope | Eligible to be routed over the public internet.
All Multicast addresses start with ffxy. y (4 bits) indicates the scope.