## Slide 1: Selected Topics on IoT Networking
6LoWPAN Address Compression

## Slide 2: IPHC Encoding (So far)
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
|Version| Traffic Class | Flow Label |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Payload Length | Next Header | Hop Limit |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| |
+ +
| |
+ Source Address +
| |
+ +
| |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| |
+ +
| |
+ Destination Address +
| |
+ +
| |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
+---+---+---+---+---+---+---+---+---+---+---+---+---+---+---+---+---+---+---+
| 0 | 1 | 1 | TF |NH | HLIM |CID|SAC| SAM | M |DAC| DAM | (inline...)
+---+---+---+---+---+---+---+---+---+---+---+---+---+---+---+---+---+---+---+

## Slide 3: Address Compression
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
|Version| Traffic Class | Flow Label |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Payload Length | Next Header | Hop Limit |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| |
+ +
| |
+ Source Address +
| |
+ +
| |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| |
+ +
| |
+ Destination Address +
| |
+ +
| |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
+---+---+---+---+---+---+---+---+---+---+---+---+---+---+---+---+---+---+---+
| 0 | 1 | 1 | TF |NH | HLIM |CID|SAC| SAM | M |DAC| DAM | (inline...)
+---+---+---+---+---+---+---+---+---+---+---+---+---+---+---+---+---+---+---+

## Slide 4: Stateless Address Compression
Stateless Compression: Make some assumptions about the Network Part of the IPv6 address.
Unicast addresses assumed link-local
The network part of a Link-Local address is always 64 bits
… and equals a known pattern, eg fe80:0000:0000:0000
Sometimes we can also assume something about the host part
fe80::0000:8a2e:370:7334
Multicast addresses: Assume something about a number of most significant (high) bytes.
Example: Assume high 120 bits equal to ff02:<24 zeros>:00
ff02::00nn

## Slide 5: Stateful (Context-based) Address Compression
Context: The network part when not fe80::
Example context: fd00::/64
Nodes assumed to share knowledge about contexts
  Often hard-coded in firmware
  Distribution of contexts out of scope of 6LoWPAN (some interesting politics here…)
  Up to 16 contexts are supported
Example. All nodes know that :
Context 0=fd00::/64
Context 1=2001:db8:85a3::/48
Instead of including the network part in a packet, we include the Context ID

## Slide 6: Source Address Compression CID, SAC and SAM
SAC
SAM
SAM
Full address inline
0: Stateless
1: Stateful
00
+---+---+---+---+---+---+---+---+---+---+---+---+---+---+---+---+---+---+---+
| 0 | 1 | 1 | TF |NH | HLIM |CID|SAC| SAM | M |DAC| DAM | (inline...)
+---+---+---+---+---+---+---+---+---+---+---+---+---+---+---+---+---+---+---+
+---+---+---+---+---+---+---+---+---+---+---+---+---+---+---+---+---+---+---+---+
|CID|SAC| SAM | M |DAC| DAM | (entire address inline...)
+---+---+---+---+---+---+---+---+---+---+---+---+---+---+---+---+---+---+---+---+
| 0 | 0 | 0 0 | M |DAC| DAM | fe| 80| 00| 00| 00|...| 8a| 2e| 03| 70| 73 |34|
+---+---+---+---+---+---+---+---+---+---+---+---+---+---+---+---+---+---+---+---+
Entire address inside the packet. No compression, really…

## Slide 7: Source Address Compression CID, SAC and SAM
SAC
SAM
SAM
Full address inline
0: Stateless
1: Stateful
00
+---+---+---+---+---+---+---+---+---+---+---+---+---+---+---+---+
|CID|SAC| SAM | M |DAC| DAM | (64 host part bits of the address inline...)
+---+---+---+---+---+---+---+---+---+---+---+---+---+---+---+---+
| 0 | 0 | 0 1 | M |DAC| DAM | 00| 00| 8a| 2e| 03| 70| 73 |34|
+---+---+---+---+---+---+---+---+---+---+---+---+---+---+---+---+
fe80::<64 bits inline>
01
Only host part inside the packet. Network assumed fe80::/64 Saved 64 bits
Example: fe80::0000:8a2e:370:7334

## Slide 8: Source Address Compression CID, SAC and SAM
SAC
SAM
SAM
Full address inline
0: Stateless
1: Stateful
00
+---+---+---+---+---+---+---+---+---+---+
|CID|SAC| SAM | M |DAC| DAM | (16 host part bits of the address inline...)
+---+---+---+---+---+---+---+---+---+---+
| 0 | 0 | 1 0 | M |DAC| DAM | 73 |34|
+---+---+---+---+---+---+---+---+---+---+
fe80::<64 bits inline>
01
fe80::ff:fe00:XXXX
10
High bits assumed fe80::ff:fe00:/112 Saved 112 bits

## Slide 9: Source Address Compression CID, SAC and SAM
SAC
SAM
SAM
Full address inline
0: Stateless
1: Stateful
00
+---+---+---+---+---+---+---+---+
|CID|SAC| SAM | M |DAC| DAM |
+---+---+---+---+---+---+---+---+
| 0 | 0 | 1 1 | M |DAC| DAM | Nothing here...
+---+---+---+---+---+---+---+---+
fe80::<64 bits inline>
01
fe80::ff:fe00:XXXX
10
High bits assumed fe80::/64
Low bits assumed SLAAC We can get those from the MAC Source Address!
Source IPv6 entirely omitted
Saved 128 bits!
fe80::<64 computed>
11

## Slide 10: Source Address Compression Stateful
SAC
SAM
SAM
0: Stateless
1: Stateful
::(Unspecified)
00
<context>::<64 inline>
01
<context>::ff:fe00:XXXX
10
<context>::<64 computed>
11
+---+---+---+---+---+---+---+---+
|CID|SAC| SAM | M |DAC| DAM |
+---+---+---+---+---+---+---+---+
| 0 | 1 | 0 0 | M |DAC| DAM |
+---+---+---+---+---+---+---+---+
Corner case: The source address is what we call “The unspecified address”, equal to all zeros.

## Slide 11: Source Address Compression Stateful
SAC
SAM
SAM
0: Stateless
1: Stateful
::(Unspecified)
00
<context>::<64 inline>
01
<context>::ff:fe00:XXXX
10
<context>::<64 computed>
11
+---+---+---+---+---+---+---+---+
|CID|SAC| SAM | M |DAC| DAM |
+---+---+---+---+---+---+---+---+
| 1 | 1 | n n | M |DAC| DAM | Context ID (4 bits) before any inline address bits
+---+---+---+---+---+---+---+---+

## Slide 12: Source Address Compression Full Picture
SAC
SAM
SAM
Full address inline
0: Stateless
1: Stateful
00
fe80::<64 bits inline>
01
fe80::ff:fe00:XXXX
10
fe80::<64 computed>
11
::(Unspecified)
00
<context>::<64 inline>
01
<context>::ff:fe00:XXXX
10
<context>::<64 computed>
11
SAM=01: XXXX carried inline
SAM=11: 64 bits computed from the respective EUI-64 address in the .15.4 frame, as if we were doing SLAAC

## Slide 13: Dest Address Compression M, DAC and DAM
‘M’ (multicast)=0:
The destination address is a unicast address.
Compression is identical to source address compression, except:
  DAM=1, DAC=00: This combination is reserved and may not be used
  Where bits are computed, they are computed based on the destination EUI-64 address of the .15.4 frame
‘M’ (multicast)=1:
The destination address is a multicast address

## Slide 14: Multicast Dest Compression M=1
DAC
DAM
DAM
Full address inline
0: Stateless
1: Stateful
00
ffXS::00GG:GGGG:GGGG 48 bits inline: Flags, Scope, Group ID
01
ffXS::GG:GGGG 32 bits inline: Flags, Scope, Group ID
10
ff02::00GG 8 bits inline: Group ID
11
ffXX:XXLL:<PP bits>:XXXX:XXXX
00
Reserved
01
Reserved
10
Reserved
11
M=1
LL and PP from context
That’s the most common one