## Slide 1: Selected Topics on IoT Networking
RPL DODAG Maintenance

## Slide 2: Types of Traffic
Multi-Point to Point (MP2P)
(or “Upwards” / “Up”)
RPL is optimised for this traffic type
A
C
B
E
F
D
Root

## Slide 3: Types of Traffic
Point to Multi-Point (P2MP)
(or “Downwards” / “Down”)
Optional
A
C
B
E
F
D
Root

## Slide 4: Types of Traffic
Point to Point (P2P)
(Up, then Down)
Worst case: All the way too the root, then down again
A
C
B
E
F
D
Root

## Slide 5: RPL Messages
DIS: DODAG Information Solicitation
  Request for DODAG information. Sent by new nodes searching for a network to join
DIO: DODAG Information Object
  Advertises node rank and other DODAG parameters
  Used to construct the DODAG / “Up” paths
  Can be multicast or unicast
  Sent periodically for DODAG topology maintenance. DIS messages trigger DIOs
DAO: Destination Advertisement Object
  Used to construct “Down” paths
DAO-ACK: An Acknowledgement of a DAO

## Slide 6: DODAG Construction Example
Remember our PHY topology
Node C sends a DIS, requesting DODAG information
DISs are multicast. Will be received by all of C’s neighbours: A, B, D, F
Assume A replies first
A
C
B
E
F
D

## Slide 7: DODAG Construction Example
D, E, F removed for simplicity
A responds with DIO
  Includes A’s rank
C chooses A as its DODAG parent and computes own Rank
If A-C link metric is 184 then C’s rank is 312
A
C
B
Rank: 128
312
184

## Slide 8: DODAG Construction Example
Later on, B sends a DIO
If the B-C link metric is 56 then C will switch to using B as preferred parent
C’s new rank decreased
A
C
B
Rank: 128
248
192
Link Metric = 56
184

## Slide 9: Modes of Operation
RPL defines Modes of Operation (MOPs)
MOP 0: Upwards routing only
MOP 1: Non-Storing Mode (Downwards routing supported, without routing tables)
MOP 2: Storing Mode (Downwards routing supported, with routing tables)
MOP 3: Storing Mode, with Multicast Support (MOP 2 + multicast routing)

## Slide 10: Downwards route construction
DAOs used to advertise “down” reachability information
DAOs travel up the DODAG
Example DAO flow:
  F to D: You can reach me
  D to B: You can reach F via me
  B to A: You can reach F via me
In MOPs 2 and 3 devices will use DAOs to populate routing tables with “down” paths.
A
C
B
E
F
D

## Slide 11: Downwards route changes No-Path DAO
Assume F switches its preferred parent from D to C.
New DAOs sent to register the new path.
A
C
B
E
F
D

## Slide 12: Downwards route changes No-Path DAO
But we also need to de-register the old path: F is no longer reachable via D
No-Path DAOs sent to indicate a path should be deleted
Example No Path DAO flow:
F to D: You can not reach me
D to B: You can no longer reach F via me
B to A: You can no longer reach F via me
A
C
B
E
F
D

## Slide 13: Routing Tables with RPL
Upwards routing:
  Easy – All we need is a default route. Basically our preferred parent.
  Populated based on DIOs
Downwards:
  Less easy – we need a separate path to every child and child’s children and so on. Q: How well does this scale in large networks?
  Created with DAOs, Deleted with No-Path DAOs
Destination | Next Hop
2001:db8:85a3::8a2e:370:7334 | fe80::8a2e:370:7334
[... more down entries ...] | 
::/0 | fe80::2:0370:00be
Special v6 address: Indicates the default route
Note: Next Hops Have to be Link-Local (Why?)
Not a link-local (Why?)