## Slide 1: MAC Sublayer ALOHA

## Slide 2: Purpose of the MAC Sublayer
A network link can be:
  Point-to-point
  Broadcast
In a broadcast network, we need:
  A mechanism to decide which device gets to transmit next
  A device needs to decide whether a received frame is for me (then process it) or someone else (then ignore it)
MAC is part of layer 2
Alternative terms: Multiple Access / Random Access / Shared Medium

## Slide 3: Where do we encounter MAC?
Especially important in LANs and wireless comms
WANs usually use point-to-point links (Satellite links are an exception)

## Slide 4: Static/Dynamic Channel Allocation
Static allocation
  Traditionally capacity of the channel is split among multiple competing users (e.g., TDM or FDM).
  Example: FM radio stations.
  Poor performance under bursty traffic
  Allocation to a user may go unused
Dynamic allocation
  Gives access to users when they need it.
  Can improve efficiency, performance and channel utilisation.

## Slide 5: Pure ALOHA
Users transmit when they have data
Retry after random time after collisions
Efficient. Low delay under low load
Collision
Collision
Time

## Slide 6: Slotted ALOHA
Synchronises senders to time slots
Twice as efficient compared to pure ALOHA