## Slide 1: CSMA (without or with CD) & Collision-Free Protocols

## Slide 2: Carrier Sense Multiple Access (CSMA)
What if we sense the channel before TX?
1-persistent CSMA. Sense the channel, then:
  If channel free, transmit
  If channel busy, keep sensing till free, then send immediately (greedy)
Non-persistent CSMA. Sense the channel:
  If channel free, transmit (same as 1-persistent)
  If channel busy, wait random time before retrying

## Slide 3: Carrier Sense Multiple Access (CSMA)
p-persistent CSMA – Slotted designs only
  If channel free, TX with probability p. Or wait for next time slot with probability 1-p. At the start of the next time slot apply the same logic.
  If channel busy, wait for a random period of time

## Slide 4: Persistent & Nonpersistent CSMA
CSMA outperforms ALOHA. Less persistent (lower p), better performance under high load.

## Slide 5: CSMA with Collision Detection
CSMA/CD improvement: Early abort of TX if a collision is detected

## Slide 6: Collision-Free protocols
Avoid collisions altogether
Senders must know when to TX
Examples:
  Bitmap
  Token Ring
  Binary Countdown
Station
Direction of
transmission
Token
Token ring