## Slide 1: Selected Topics on the IoT
MQTT Sessions and Messages

## Slide 2: Core Elements
MQTT Session
Application
TCP
MQTT
Client
Client:
Subscriber or Publisher
Can be both
TCP
MQTT Server (Broker)
Subscriptions
Topic A
Topic B
Topic C
TCP Connection
TCP/IP

## Slide 3: MQTT Session Lifecycle
(Time)
Establish TCP Connection (3-way Handshake)
Tear Down TCP Connection (2-way Termination)
CONNECT
CONNACK
Client
Broker
(Multiple Subscribe and Publish Messages)
DISCONNECT

## Slide 4: Simple Exchange
SUBACK
SUBACK
(Time)
PUBLISH
Publisher
TCP Connection and MQTT Session already established
Subscribers
SUBSCRIBE
PUBACK (optional)
PUBLISH
SUBSCRIBE
PUBLISH
PUBACK (optional)
PUBLISH
PUBLISH

## Slide 5: Quality of Service Levels
Additional layer of reliability on top of TCP
  SUBACK and CONNACK are not optional and are not related to QoS.
QoS0: At most once delivery
  When it’s lost, it’s lost
QoS1: At least once delivery
  PUBACK messages are used to confirm that a Publish was received by the broker. (see optional PUBACK in previous slide)
  Publisher will retry after timeout
QoS2: Exactly once delivery
  QoS1 + No duplicates
  Complex control message flow

## Slide 6: More Message Types
PUBREC, PUBREL, PUBCOMP
Used with QoS2 only
UNSUBSCRIBE, UNSUBSCRIBEACK
Terminate an existing subscription
PINGREQ, PINGRESP
“Are you alive?”, “Yes, I am”
Each session has a “keep alive” time (set in CONNECT message). It specifies the max interval between messages from the client.
PINGREQ used to refresh keep alive timer when no other messages are present.

## Slide 7: Publish Message Triggers
Q: What triggers a publish?
A: Decided exclusively by the logic on the publisher and is topic-dependent. The subscriber has no control and cannot request a publish.
Examples (Combinations are possible):
Periodic (e.g. every X secs/mins)
Sudden change (e.g. reading is +/- 10% compared to previous reading)
Thresholds (e.g. reading is outside a normal range)