## Slide 1: Selected Topics on the IoT
CoAP Messages

## Slide 2: HTTP GET Resource Example
          HTTP/1.1 200 OK\r\n [headers]
          \r\n
          25.38oC
Establish TCP Connection (3-way Handshake)
(Time)
Tear Down TCP Connection (2-way Termination)
    GET /temp HTTP/1.1\r\n
    [headers]\r\n
    \r\n

## Slide 3: CoAP GET Resource Example
          2.05
          text/plain
          25.38C
(Time)
    GET /temp

## Slide 4: Is, Is Not
CoAP is
Efficient design
Suitable for constrained devices
Easy to proxy to/from HTTP
CoAP is NOT a replacement for HTTP.
CoAP is NOT a method for HTTP compression.

## Slide 5: CoAP Methods
GET: Read resource from server
POST: Update or Create Resource (Usually, but not necessarily)
PUT: Update or Create Resource
DELETE: Delete Resource on Server
Similar to HTTP!

## Slide 6: PUT vs POST
PUT is “indempotent”
  Two identical PUT requests have the same outcome
POST is not indempotent
  Two identical POSTs requests may result in different outcomes
Same applies for HTTP PUT & POST

## Slide 7: CoAP Uses URLs
scheme: coap
server: [fdfd::1] (this is an IPv6 address)
port: 5683 (Default for CoAP. Can be omitted)
resource path: /sen/temp
query: v=1
coap://[fdfd::1]:5683/sen/temp?v=1

## Slide 8: Response Codes
2.xx: Success
4.xx: Client Error
5.xx: Server Error
Some Examples:
  2.01 Created
  2.05 Content
  4.00 Bad Request
  4.02 Bad Option
  5.00 Internal Server Error
  5.03 Service Unavailable
Again, HTTP Similarities!

## Slide 9: Compact Messages
CoAP Messages are compact
“Request method and Response code do not appear as clear text in messages”
CODE field in the header: 8 bits. Used to specify method (requests) as well as response code
Some Examples:
1: GET
2: POST
65: 2.01 Created
69: 2.05 Content